## Slide 1: Way forward on UE demodulation enhancement for HST
NTT DOCOMO, INC.
3GPP TSG-RAN WG4 Meeting #90 Athens, GR, 25th Feb – 1st March, 2019
R4-1902521

## Slide 2: Background
The core part of this WI include
Extend the RRM/demodulation enhancement to CA scenario [RAN4/RAN2]
  At least, extend Rel-14 RRM/demodulation enhancement to CA case
The following new scenario are considered [RAN4]
  The target speed is 500km/h
  SFN scenario defined in TS36.101 and TR36.878 with bidirectional coverage for tunnel and open space
  SFN scenario defined in TS36.878 with unidirectional coverage for tunnel and open space
    More discussion on how to specify the general unidirectional antenna pattern
  In addition to SFN scenarios, other deployment scenarios are not precluded
Evaluate the downlink and uplink demodulation performance under the above scenarios, using the existing LTE CRS/DMRS, and study the enhancement of the downlink and uplink demodulation under those scenarios [RAN4]
  New or modified physical layer reference signals shall not be considered
  Change for PRACH shall not be considered
  The maximum Doppler shift supported by the LTE CRS/DMRS transmission schemes is to be determined by RAN4
  If RAN4 identifies the necessity for enhancements, define relevant signaling support [RAN4/RAN2]

## Slide 3: Companies’ view on CA (1)
Define HST-SFN CA requirements based on Rel.14 requirements
  Ericsson, Qualcomm, NTT DOCOMO, CMCC
Not Define HST-SFN CA requirements
  Huawei, Intel, MTK

## Slide 4: Way forward on uni-directional and bi-directional HST-SFN
Demand for “bi-directional + 500km/h” scenario by CMCC and NTT DOCOMO has been observed.
Demand for “uni-directional + 500km/h” scenario, need more operators inputs.

## Slide 5: Way forward on 500km/h velocity (1)
Which HST-SFN scenario is specified:
  Option 1: Adopt HST-SFN Bi-directional scenario
    Huawei, CMCC, Intel, NTT DOCOMO, Qualcomm, MTK
    Maximum Doppler shift must be capped
    Details are FFS
  Option 2: Adopt HST-SFN Uni-directional scenario
    Ericsson, Qualcomm
    Details are FFS
  Option 3: Adopt HST-SFN Bi-directional scenario
    NTT DOCOMO
    Maximum Doppler shift cap is FFS
    Details are FFS

## Slide 6: Way forward on 500km/h velocity (2)
Whether original HST and multipath scenario are considered or not:
  Option 1: Specify HST, multipath and HST-SFN scenario
    NTT DOCOMO
  Option 2: Specify only HST-SFN scenario
    Huawei, Qualcomm, Intel, Ericsson, MTK

## Slide 7: Way forward on 500km/h velocity (3)
DMRS-based transmission modes are considered or not in this WI
  Option 1: Consider
    Huawei
  Option 2: Not consider
    Qualcomm, Intel, MTK
4Tx is not considered in this WI.
CSI is not considered in this WI.