## Slide 1: 3GPP TSG-RAN WG4 Meeting #90 Athens, Greece, 25th February – 1st March 2019
Huawei, HiSilicon, Ericsson, Qualcomm, Nokia
Way forward on RRM for Rel-16 eMTC
R4-1902552

## Slide 2: Channel quality report in Msg3
The framework of NB-IoT requirements for channel quality report in Msg3 is re-used for eMTC
The detailed requirements for eMTC are discussed based on further agreements from RAN1/2.
RAN4 to consider the difference between NB-IoT and eMTC , for example for the following aspects:
  hypothetical MPDCCH parameters and the evaluation period
  report mapping
  measurement accuracy
RAN4 to discuss whether to specify requirements for aperiodic quality report in connected mode using same quality definition as in IDLE mode Msg3 based on further agreements from RAN1/2

## Slide 3: Group WUS
RAN4 shall discuss whether the release 15 WUS requirements can be reused for release 16 legacy WUS and whether new requirements are needed for release 16 UE-group WUS based on the RAN1/RAN2 agreements.

## Slide 4: MPDCCH performance improvement
RAN4 is to discuss whether to define new RLM requirements and/or test cases for UEs capable of using CRS and DMRS for MPDCCH demodulation if significant gain is achieved compared to Rel-13 MPDCCH demodulation (DMRS based)

## Slide 5: Stand-alone deployment
RAN4 is to discuss whether to define new RLM requirements and/or test cases for UEs operating under standalone deployment, i.e. using LTE control region for MPDCCH transmission.

## Slide 6: Preconfigured UL resource
RAN4 is to discuss whether to specify requirements for following methods to validate TA
  Serving cell change
  Time alignment timer (TAT)
  serving cell RSRP change
FFS if RAN4 should define criteria for TA validity, e.g. threshold for the RSRP change, threshold for the TA change, threshold for the time period during which TA is considered as valid

## Slide 7: Extreme coverage for non-BL UE
RAN4 is to discuss the potential RRM work for extreme coverage improvement for non-BL UE based on RAN1/2 outcome.

## Slide 8: Mobility enhancement
RAN4 shall evaluate the performance of RSS based RRM measurement based on agreed simulation assumptions.
  RSS measurements are studied for IDLE mode, and it is FFS for CONNECTED mode
The serving cell monitoring relaxation defined for Rel-15 NB-IoT can be used as a starting point for eMTC. RAN4 should analyze the difference between NB-IoT and eMTC before defining the requirements.