## Slide 1: Motivation for new WI on NR performance requirement enhancement
China Telecom
April 2019
3GPP TSG-RAN WG4 Meeting #90bis
Xi'an, China, 8th - 12th April 2019
Agenda: 13
R4-1902844

## Slide 2: General motivation
With the very tight time schedule for NR Rel-15 performance work, several important NR features specified in Rel-15 core part are not covered when developing the Rel-15 performance requirements, such as:
  UE and BS receivers for handling inter-cell, inter-layer or inter-user interference
  PDSCH CA and EN-DC demodulation requirements
  Meanwhile, these features are very important Rel-15 features, and some operators have plans to deploy them in the early deployments.
Thus it is proposed to open a new Rel-16 WI to define performance requirements for the selected NR features that are specified in Rel-15 core part but not covered in Rel-15 performance part.

## Slide 3: Interference-aware receivers (1/2)
  Motivation
  Co-channel interference has substantial impact on DL and UL performance.
  In LTE, several interference-aware receivers have been introduced for data channel throughput improvement, and some of them have no impact on core specification:
    PDSCH: inter-cell interference rejection combining (IRC), inter-stream interference cancellation (IC) [1]
    PUSCH: inter-cell IRC, intra-cell inter-user IC [2]
  In NR Rel-15,
    PDSCH and PUSCH performance requirements are defined without explicit modeling of inter-cell interference, i.e., inter-cell IRC is not considered [3] [4].
    Meanwhile, PUSCH performance requirements are defined without considering intra-cell inter-stream/user interference handling [3].
  In NR NOMA SI [5], two main classes of receiver architecture are considered based on linear filters with IC for handling intra-cell inter-user interference
    Low complexity: hard-IC (hard L-CWIC)
    Medium complexity: hybrid-IC (mixing hard-IC and soft-IC/turbo L-CWIC)
  It is an efficient way to improve NR spectral efficiency by employing interference-aware receiver.

## Slide 4
  Propose to consider performance requirements with the following receivers:
  BS side:
    PUSCH requirements with enhanced receivers for handling co-channel inter-cell interference
      LMMSE-IRC or interference pre-whitening can be considered as reference receiver
    Study to introduce PUSCH requirements with enhanced receivers for handling co-channel intra-cell inter-stream/user interference
      For intra-cell inter-user interference handling, hard-IC (hard L-CWIC) and hybrid-IC (mixing hard-IC and soft-IC) receivers as defined in NOMA TR 38.812 can be considered as reference receiver
  UE side:
    PDSCH requirements with enhanced receivers for handling co-channel inter-cell interference
      LMMSE-IRC or interference pre-whitening can be considered as reference receiver
    Study to introduce PDSCH requirements with enhanced receivers for handling co-channel intra-stream interference for SU-MIMO
      Up to 4 transmission layers for SU-MIMO are to be considered, and parallel - soft IC can be considered as reference receiver
  Interference-aware receivers (2/2)

## Slide 5: CA and EN-DC requirements
  Motivation
  In Rel-15, the RF requirements has been specified for both intra-band and inter-band NR CA [6].
  However, for the performance part, only some SDR requirements are defined for NR CA, while the other requirements for NR CA has been de-prioritized [7].
  To verify the correct implementation of NR CA feature, PDSCH normal demodulation requirements for CA needs to be defined.
  Propose to consider the following performance requirements:
  UE side: PDSCH normal demodulation requirements and CA/EN-DC specific requirements, e.g., soft buffer management, power imbalance.

## Slide 6: Proposal and scope
The general objective is to define performance requirements for the selected NR features that are specified in Rel-15 core part but not covered in Rel-15 performance part.
The main objectives are as follows:
  Consider the features listed in slide #3 to #5, and make further down-selection and/or prioritization among them if needed.

## Slide 7: References
[1] TS 36.101, E-UTRA User Equipment (UE) radio transmission and reception
[2] TS 36.104, E-UTRA Base Station (BS) radio transmission and reception
[3] R4-1813942, WF for NR PUSCH demodulation, Nokia, Nokia Shanghai Bell, RAN4 #88bis, Oct 2018.
[4] R4-1814239, Simulation assumptions for NR PDSCH demodulation performance requirements, Intel, RAN4 #88bis, Oct 2018.
[5] RP-182478, TR 38.812 v1.0.0 on Study on Non-Orthogonal Multiple Access (NOMA) for NR, ZTE, RAN #82, Dec 2018.
[6] TS 37.865-01-01, NR Carrier Aggregation for intra-band (m Down Link (DL) / 1 Up Link (UL) bands) and inter-band (n Down Link (DL) / 1 Up Link (UL) bands)
[7] R4-1814238, Way forward on NR UE PDSCH demodulation requirements and General aspects, Intel, RAN4 #88bis, Oct 2018.

## Slide 8
Thanks!