## Slide 1: Way forward on UE demodulation enhancement for HST
Qualcomm Inc, ...
3GPP TSG-RAN WG4 Meeting #90-Bis Xi’an, China, 8 – 12 April, 2019
R4-1903287
Document for: Approval

## Slide 2: Background
A WF on UE demod enhancement for HST was agreed in last meeting (R4-1902521)
On each topic, different options were tabled
In this WF, down-selection of options for each topic is proposed to help progress demod work

## Slide 3: Extension of demod requirements to CA
Define HST-SFN CA requirements based on Rel.14 requirements
  Ericsson, Qualcomm, NTT DOCOMO, CMCC
Not Define HST-SFN CA requirements
  Huawei, Intel, MTK
NOTE: This is aligned with extension of RRM requirements to CA and also in agreement with carriers that have HST deployments

## Slide 4: Way forward on 500km/h velocity (1)
Which HST-SFN scenario is specified:
  Option 1: Adopt HST-SFN Bi-directional scenario
    Huawei, CMCC, Intel, NTT DOCOMO, Qualcomm, MTK
    Maximum Doppler shift must be capped
    Details are FFS
  Option 2: Adopt HST-SFN Uni-directional scenario
    Ericsson, Qualcomm
    Details are FFS
  Option 3: Adopt HST-SFN Bi-directional scenario
    NTT DOCOMO
    Maximum Doppler shift cap is FFS
    Details are FFS
NOTE: Technical analysis supported by simulation results justify elimination of Option 3

## Slide 5: Way forward on 500km/h velocity (2)
Whether original HST and multipath scenario are considered or not:
  Option 1: Specify HST, multipath and HST-SFN scenario
    NTT DOCOMO
  Option 2: Specify only HST-SFN scenario
    Huawei, Qualcomm, Intel, Ericsson, MTK
NOTE: HST-SFN is aligned with typical field deployments

## Slide 6: Way forward on 500km/h velocity (3)
DMRS-based transmission modes are considered or not in this WI
  Option 1: Consider
    Huawei
  Option 2: Not consider
    Qualcomm, Intel, MTK
NOTE: With current DMRS arrangement in a subframe, channel estimation significantly degrades in high Doppler conditions