## Slide 1: WF on Scell Activation Delay in FR2
Qualcomm
R4-1904696

## Slide 2: Agreements
Agreement
  L1-RSRP/L3-RSRP report during SCell activation or L3-RSRP report before SCell activation will be performed by the UE to help network to decide the active TCI.
Scell known condition for FR2
  Option 1: For the first SCell activation in FR2 bands, if UE reports the L3-RSRP with beam index within last [Xms] for a cell, and the active TCI is selected based on UE report, then that cell can be viewed as known cell
    A NR cell in FR2 is said to be known if it meets the following conditions:
      During the period equal to [X ms]:
        the UE has sent a valid measurement report for the cell and
        the cell remains detectable according to the cell identification conditions
      The SSB measured during the period equal to [Y ms] also remains detectable during the SCell activation delay according to the cell identification conditions specified in section 9.2 and 9.3.
      FFS on X and Y values.
      If X and Y cannot be concluded in R15, then only unknown cell condition will apply for R15.

## Slide 3: Agreements
Implication of known cell definition
  SCell activation delay will not include the L1-RSRP reporting time
  UE knows coarse timing of the cell
    Does not need to perform search again as part of activation procedure
Starting point of SCell activation
  MAC-CE command for SCell activation
Ending point of SCell activation
  Valid CQI reporting

## Slide 4: Activation Procedure (for information)
UE needs to know the TCI state as part of SCell activation
For a unknown cell, follow procedure is assumed
  gNodeB sends SCell activation command
  UE reports L1-RSRP
  gNodeB send TCI state activation command
  gNodeB indicate UE which CSI-RS to use for CQI reporting
  UE reports valid CQI
For a known cell, gNodeB can send both SCell activation and TCI state activation commands at the same time.
  gNodeB indicate UE which CSI-RS to use for CQI reporting
  UE report valid CQI

## Slide 5: Definition of Scell Activation Time (for information)
SCell activation time to consist of potential following times
  TMAC-CE,SCell Activation
  TMAC-CE,TCI Activation
  TAGC
  TCellSearch
  TL1-RSRP
  TFineTiming
  TCSI_Reporting

## Slide 6: Scell Activation Times (for information)
Components needed in known and unknown cases
Procedure | Known | unknown
TMAC-CE,SCell Activation | Yes | Yes
TMAC-CE,TCI Activation | Yes | Yes
TL1-RSRP | No | Yes
TFineTiming | Yes | TBD
TCSI_Reporting | Yes | Yes
TCellSearch | No | Yes
TAGC | No | Yes