## Slide 1: 3GPP TSG-RAN WG4 Meeting #90bis Xi’an, China, 8th – 12th April, 2019
Ericsson, Qualcomm Incorporated, Huawei, Nokia, Nokia Shanghai Bell
Way forward on Rel-16 MTC RRM enhancement
R4-1904806

## Slide 2: Channel quality report in Msg3
MPDCCH parameter for DL quality report in Msg3 is re-used from RLM, expect maximal repetition level and aggregation level.
    If the repetition number in DL quality information is larger than 1, the MPDCCH aggregation level is 24.
    If the repetition number in DL quality information equals to 1, wait for RAN1 decision to determine the maximal MPDCCH repetition level and aggregation level.
RAN4 waits for further RAN1/RAN2 agreements for other work on DL channel quality report.

## Slide 3: Group WUS
RAN4 shall wait for further RAN1 progress on release 16 WUS design work to decide whether release 15 WUS requirements are reusable.

## Slide 4: MPDCCH improvement on RLM
It is possible to achieve significant MPDCCH BLER performance gain by using DMRS and CRS for MPDCCH demodulation.
RAN4 shall evaluate the MPDCCH BLER performance based on RAN1 agreement on precoder options

## Slide 5: Preconfigured UL resource
Serving cell RSRP change based TA validation
  The value(s) for the threshold(s) used for validating the TA are up to network implementation
  Following options can be considered:
    Option 1: Using relative RSRP change together with TA change or DL/UL timing change
    Option 2: applying PUR only in normal coverage considering decreased RSRP accuracy in enhanced coverage.
    Option 3: using only relative RSRP change against signaled threshold(s)
  RAN4 is to study how PUR transmissions are aligned with configured DRX/eDRX and its impact on the synchronization state to perform PUR transmission.

## Slide 6: Mobility enhancement
RAN4 prioritizes the work on defining the measurement requirements for RSS based RSRP measurements for IDLE mode.
Based on RSS based RSRP measurement performance gain, RAN4 to discuss whether RSS can be used for improving the CE level selection when multiple CE levels are configured in random access procedure.

## Slide 7: Mobility enhancement
For relaxed serving cell monitoring
  The condition for enabling relaxed serving cell monitoring is directly re-used from NB-IoT. The relaxation factor for eMTC can be defined in the same way as NB-IoT by replacing DRX cycle length {1.28, 2.56, 5.12, 10.24} with {0.32, 0.64, 1.28, 2.56}.
  The same principle to derive the time period of T0 as in NB-IoT is reused where relaxed serving cell monitoring is not allowed.