## Slide 1: 3GPP TSG-RAN WG4 Meeting #90bis Xi’an, China, 8th – 12th April 2019
Huawei, HiSilicon, Ericsson, Qualcomm, Nokia
Way forward on RRM impact of the R16 enhancement for NB-IoT
R4-1904807

## Slide 2: Group WUS
RAN4 shall wait for further RAN1 progress on release 16 group WUS design to decide whether release 15 WUS requirements can be reused

## Slide 3: Preconfigured UL resource
Serving cell NRSRP change based TA validation
  The value(s) for the threshold(s) used for validating the TA are up to network implementation
  Following options can be considered:
    Option 1: Using relative NRSRP change together with TA change or DL/UL timing change
    Option 2: applying PUR only in normal coverage considering decreased NRSRP accuracy in enhanced coverage.
    Option 3: using only relative NRSRP change against signaled threshold(s)
  RAN4 is to study how PUR transmissions are aligned with configured DRX/eDRX and its impact on the synchronization state to perform PUR transmission.

## Slide 4: Msg3 based channel quality reporting
Legacy requirements defined for R14 msg3 based quality reporting apply for msg3 based quality reporting on non-anchor carriers including,
  Hypothetical NPDCCH and
  Report mapping and
  Reporting accuracy
  FFS T1 and T2

## Slide 5: NRS presence on non-anchor carriers
Define non-anchor carrier serving cell RRM requirements based on NRS measurement on the non-anchor carrier in TS 36.133.
If configured by the network, serving cell non-anchor carrier measurements are feasible provided that
  the relaxed cell monitoring criteria defined in TS 36.306 are met, and
  transmit power difference of the signals/channels between anchor- and non-anchor carriers is known to the UE, and
  UE is not configured with any positioning measurements and there are sufficient number of NRS subframes available for measurements as being discussed in RAN1
FFS if the RSRP/RSRQ offset is used to compensate the measurement result towards non-anchor carriers