## Slide 1: WF on Pcmax for inter-band NE-DC
InterDigital

## Slide 2: Background from online discussions The following statements were agreed in the main session
It is common understanding that for DPS UE, LTE power will NOT be scaled regardless whether NR is configured as MCG (NE-DC) or SCG (EN-DC)
It further agreed that for NE-DC, for given Plte, NR can be scaled even down to zero if Plte + Pnr >[=] Ptotal
No test case for Plte + Pnr > Ptotal
The test case(s) is required for the case that Plte + Pnr < [=] Ptotal for overlapping cases.

## Slide 3: Discussion
It further agreed that for NE-DC, for given Plte, NR can be scaled even down to zero if Plte + Pnr >[=] Ptotal
  This means literally that we can use Pcmax_L_LTE for lower limit of the Pcmax_L-NE-DC.
The test case(s) is required for the case that Plte + Pnr < [=] Ptotal for overlapping cases.
  This will lead to a normal calculation of Pcmax_L-NE-DC that considers both NR and LTE lower limits.

## Slide 4: Proposal
PCMAX_ NE-DC _H(p,q) = MIN {10 log10 [pCMAX H _ E-UTRA,c (p) + pCMAX H,f,c,NR c(q)], PEMAX, NE-DC ,PPowerClass, NE-DC}
And:
If 10 log10 [pCMAX E-UTRA,c (p) + pCMAX c,,NR c(q)] > MIN { PEMAX, NE-DC ,PPowerClass, NE-DC}
Then
// When NR scaling occurs
PCMAX_ NE-DC _L(p,q) = MIN {10 log10 [pCMAX L _ E-UTRA,c (p) ], PEMAX, NEDC ,PPowerClass, NE-DC}
Else
// PCMAX_ NE-DC _L(p,q) = MIN {10 log10 [pCMAX L _ E-UTRA,c (p) + pCMAX L,f,c,,NR c(q)], PEMAX, NE-DC ,PPowerClass, N-DC}

## Slide 5: References
R4-1903088 Inter-band NE-DC - Pcmax requirement definition, InterDigital
R4-1902920 Configured output power for inter-band NE-DC, Intel
R4-1904465 Draft CR for 38.101-3 inter-band NE-DC Pcmax, Huawei