## Slide 1: WF on LTE/NR spectrum sharing in Band 41/n41
KDDI
3GPP TSG-RAN WG4 #90-bis Meeting
Xi’an, China, 8th Apr. – 12th Apr., 2019
R4-1905190

## Slide 2: Background
A WF [2] is approved for the compatible issue of Rel-15 UE for band 41/n41 spectrum sharing in RAN4#90.
To solve the compatibility issue of sulotion#2, verify feasibility of the following alternative plans
Alternative#1: apply the following RRC information to n41 and clarify the UE behavior in Rel-15 to prevent UE without UL 7.5kHz frequency shift to access to spectrum sharing NW of n41
  One company declared that this proposal is a NBC (non backward compatibility change).
Alternative#2: deploy SSB of spectrum sharing NW where Rel-15 UE cannot find it. For spectrum sharing, we need to enable repetition of sync raster (M=1,3,5) in Rel-16 which has more sync raster entries compared to Rel-15.
  Feasibility of this proposal needs to be further verified and it will make constrains on operator’s NW deployment.
Alternative#3: other solutions are not precluded

## Slide 3: Possible options for Rel-15 UE compatible issue (1/2)
Option1: From Rel-15, the UE mandatory support the UL 7.5kHz shift and 100kHz channel raster.
Option2: From Rel-16, the UE mandatory support the UL 7.5kHz shift, 100kHz channel raster and specify the Rel-15 UE behavior to prevent Rel-15 UE to access the band n41 cell with 7.5kHz UL shift configuration
Option 3: From Rel-16, the UE mandatory support the UL 7.5kHz shift and 100kHz channel raster. Reuse band n41 and introduce support for DSS
  DSS support: UL 7.5kHz shift, 100kHz channel raster
  Deploy SSB at SS raster positions where Rel-15 UE can not find it to prevent Rel-15 UE from accessing spectrum sharing NW
  It’s FFS whether Rel-16 UE mandatory supporting DSS
    For optional case, behavior of UEs that do not support DSS needs to be clarified
Notes: QC: Op1/Op2 have NBC issue.
CMCC: Op1 have NBC issue.
Softbank: Depending on the method on op2, how to configuration. Not clear how op2 operate.
Sprint: For op2, we are not talking new behavior, just place SSB to ensure legacy UE not find this cell.
Op 3a:
Nokia: Op3 still need Rel-16 Cap signaling
Softbank/CMCC/KDDI: upper to Rel-16 conclusion for this feature.
Ericsson: we would like to 100kHz channel shift will have impact SS raster. This is a generic question, we need to further discuss.
KDDI: We would like to focused on Rel-15 UE Compatibility issue.
QC: we similar comments as Ericsson, with 100kHz have impact SS raster.

## Slide 4: Possible options for Rel-15 UE compatible issue (2/2)
Option4: Reuse band n41, introduce support for DSS and use the cell barring mechanism to prevent Rel-15 UE to access band n41 cell with 7.5kHz UL shift configuration.
  Need to check feasibility from signaling perspective
  DSS support: UL 7.5kHz shift, 100kHz channel raster
  It’s FFS whether Rel-16 UE mandatory supporting DSS
    For optional case, behavior of UEs that do not support DSS needs to be clarified
Option5: From Rel-16, the UE mandatory support the UL 7.5kHz shift and Define a new band and UL 7.5kHz shift is mandatory supported in this new band
  The UE supporting new band shall also support band n41
  Apply all n41 requirements including CA and EN-DC band combinations (i.e. CA, DC, SUL) to new band
  Mandatory support of 100kHz channel raster is FFS
Notes: Qc: For all the options, only 7.5 UL shift tied with supporting 15kHz SCS.
Ericssion: we see certain impact on op4, we would like to check the feasibility of op4. In that sense, Op5 more simple, no impact on RAN2.
Sprint: Op5 do have impact on RAN2, current IE “7.5kHz shift” only applied for FDD and SUL . So we still need to do modification.
CMCC: this signaling only target from Rel-16. we do need to check the impact on this proposal.
KDDI: Op4 better check RAN2

## Slide 5: Reference
[1] RP-182883, “New WI proposal: LTE/NR spectrum sharing in Band 41/n41,” KDDI Corporation
[2] R4-1902450, “WF on LTE/NR spectrum sharing in Band 41/n41 ”, KDDI, CMCC, Sprint