## Slide 1: WF on NR PUSCH demodulation requirements
R4-1907241
Document for: Approval
3GPP TSG-RAN WG4 RAN#91
Reno, Nevada, US, 13th – 17th May 2019
Agenda: 6.12.2.2.1
Nokia, Nokia Shanghai Bell, […]

## Slide 2: Background
The following WFs were approved:
  R4-1808024, WF on NR PUSCH demodulation requirements in Rel-15, RAN4#87
  R4-1809366, WF on NR PUSCH demodulation requirements, RAN4#AH1807
  R4-1811694, WF on NR PUSCH demodulation requirements, RAN4#88
  R4-1813942, WF on NR PUSCH demodulation requirements, RAN4#88bis
  R4-1816347, WF on NR PUSCH demodulation requirements, RAN4#89
  R4-1902434, WF on NR PUSCH demodulation requirements, RAN4#90
  R4-1904717, WF on NR PUSCH demodulation requirements, RAN4#90b

## Slide 3: PTRS configuration for MCS2
FR2: PT-RS configuration for QPSK:
    No consensus is reached between the options, so there will be no test cases for MCS 2 with PT-RS enabled and FFS whether to update the applicability rule.

## Slide 4: FR2 Additional DM-RS
DM-RS configuration for FR2:
  Keep test cases with DMRS configuration 1+0 for FR2.

## Slide 5: PUSCH Notation Harmonization
Notation in TS 38.104/141-1/141-2 |  | 
Current | Proposed update | Source
Maximum number of OFDM symbols for front loaded DMRS | DM-RS duration = {single-symbol DM-RS} | TS 38.211 Table 6.4.1.1.3-5
Number of additional DMRS symbols | Additional DM-RS position= {pos0, pos1, pos2, pos3} | TS 38.331 6.3.2
EPRE ratio of PUSCH to DMRS | Ratio of PUSCH EPRE to DM-RS EPRE | TS 38.214 Table 6.2.2-1
DMRS port | DMRS port(s) | TS 38.212 Table 7.3.1.1.2-9
N_ID | N_ID^0 | TS 38.211 6.4.1.1.1.1
Time domain resource | Time domain resource assignment | TS 38.214 6.1.2.1
PUSCH starting symbol index | Start symbol | TS 38.214 6.1.2.1
PUSCH symbol length | Allocation length | TS 38.214 6.1.2.1
Frequency domain resource | Frequency domain resource assignment | TS 38.214 6.1.2.2
DMRS configuration = {1+0, 1+1} | Additional DM-RS position= {pos0, pos1} | TS 38.331 6.3.2

## Slide 6: Test Parameters, CP-OFDM
Parameter | value | 
 | FR1 | FR2
Transform precoding | Disabled | Disabled
Number of Tx | 1, 2 | 1, 2
Number of Rx | 2, 4, 8 | 2
Number of layers | 1, 2 | 1, 2
Transmission scheme | Identity matrix (TPMI index 0) | Identity matrix (TPMI index 0)
DMRS type | type 1 | type 1
Number of DMRS symbols | 1, 1+1 | 1, 1+1 (low prio)
symbols length | 14 | 10
start symbol index | 0 | 0
Time domain resource allocation type | type A and B | type B
Frequency domain resource | Full applicable test bandwidth | Full applicable test bandwidth
MCS index | 2, 16, 20 (20 only for 1Tx) | 2, 16, 20 (20 only for 1Tx)
Carrier frequency (GHz) | 4 | 30
Propagation condition | MCS 2: TDL-B 100ns, 400 Hz MCS 16: TDL-C 300ns, 100 Hz MCS 20: TDL-A 30ns, 10Hz | MCS 2: TDL-A 30ns, 300Hz MCS 16: TDL-A 30ns, 300Hz MCS 20: TDL-A 30ns, 75Hz
SCS and BW | 15kHz: 5MHz, 10MHz, 20MHz; 30kHz: 10MHz, 20MHz, 40MHz, 100MHz 60kHz(FR2): 50MHz, 100MHz; 120kHz: 50MHz, 100MHz, 200MHz | 
PTRS | Not configured | QPSK: Not configured 16 and 64 QAM: (Configured with KPTRS =2, LPTRS =1) and (not configured, low prio)
Timing offset | 0 | 0
Frequency offset | 0 | 0
Code block group, Frequency hopping, Limited buffer rate matching | Disabled | Disabled
Number of HARQ transmissions | 4 | 4
Testing metric | SNR @70% of maximum throughput | SNR @70% of maximum throughput

## Slide 7: Test Parameters, DFT-s-OFDM
Parameter | value | 
 | FR1 | FR2
Transform precoding | enabled | enabled
Number of Tx | 1 | 1
Number of Rx | 2, 4, 8 | 2
Number of layers | 1 | 1
DMRS type | type 1 | type 1
Number of DMRS symbols | 1+1, 1 | 1, 1+1 (low prio)
symbols length | 14 | 10
start symbol index | 0 | 0
Time domain resource allocation type | type A and B | type B
Frequency domain resource | 15kHz: 25 PRB; 30kHz: 24 PRB (middle of test BW) | 60kHz: 30 PRB; 120kHz: 30 PRB (middle of test BW)
MCS index | 2 | 2
Carrier frequency (GHz) | 4 | 30
Propagation condition | MCS 2: TDL-B 100ns, 400 Hz | MCS 2: TDL-A 30ns, 300Hz
SCS and BW | 15kHz: 5 MHz; 30kHz: 10 MHz | 60kHz: 50; 120kHz: 50
PTRS | Not configured | Not configured
Timing offset | 0 | 0
Frequency offset | 0 | 0
Code block group, Frequency hopping, Limited buffer rate matching | Disabled | Disabled
Number of HARQ transmissions | 4 | 4
Testing metric | SNR @70% of maximum throughput | SNR @70% of maximum throughput