## Slide 1: Way forward on NR mobility enhancement
Intel
3GPP TSG-RAN4 Meeting #91
Reno, USA, 13 – 17 May, 2019
R4-1907391
Document for: Approval

## Slide 2: Agreements on handover with simultaneous Rx/Tx with source and target cells
From RAN4 perspective, handover from one frequency range to another with simultaneous Rx/Tx is feasible, e.g. for UE supporting FR1+FR2 NR DC.
It is up to other leading group to decide if such handover is to be support or not in this work item.
Handover with simultaneous Rx/Tx with both source and target cells involving different SCS is feasible depending on UE capability.
All the existing UE capability regarding Rx/Tx with different SCS cannot be extended to cover this case. New UE capability needs to be introduced.

## Slide 3: Agreements on RACH-less handover
RACH-less handover with 0 or equal TA is feasible in FR2 if source and target cells are well synchronized.
From RAN4 perspective, if the source cell can configure multiple UL grant resources associated with different DL RS (SSB or CSI-RS) in target cell, handover successful rate can be increased.
Note this increases resource overhead in the target cell. It is up to other working group if to support this.
Feasibility of RACH-less handover with non-zero/non-equal TA is FFS. Companies are encouraged to provided further analysis.

## Slide 4: Agreements on conditional handover
The handover delay DCHO in CHO is defined from the time when handover condition is met to the time when the first PRACH preamble is transmitted. The interpretation of “handover condition is met” is:
option 1: the time when actual channel condition is satisfied (before UE realizes).
option 2: the time when UE realizes the condition is satisfied and HO is executed.
If option 1 is agreeable, then
DCHO = Ttrigger + Tinterrupt_CHO
Where:
Ttrigger: is the delay from the time when condition is met to HO is actually executed:
Ttrigger = TRRC, 1 + Tmeasure + TTTT
TRRC, 1 : CHO command RRC procedure delay. TRRC, 1 =0 if the time from when the CHO command until the time when the condition is met > RRC procedure delay, otherwise TRRC, 1 = RRC procedure delay- (time from CHO command until the condition is met)
Tmeasure: measurement cycle on the target frequency layer
TTTT: length of time-to-trigger window if configured
Tinterrupt_CHO: is the interruption time from HO is executed to the first PRACH preamble is sent to the target cell:
Tinterrupt_CHO = TRRC_2 + Tinterrupt
  TRRC_2: time to disconnect with the source cell, e.g. stop timer if running, release UL data compression configuration and etc
  Tinterrupt = Tsearch + TIU + 20+ T∆ (same as legacy definition, where Tsearch may not be needed if CHO to unknown target cell is not supported according to other working group)

## Slide 5: Appendix: example for CHO procedure (option 1)