## Slide 1: Way Forward on B41/n41 A-MPR assumptions
Sprint, Skyworks
R4-1907495

## Slide 2: Background
Objective is to assess feasibility of optional hardware improvements
  Substantial improvements in A-MPR above Rel-15 definition may be possible
  Scheduler could potentially use information that UE will take less than full Rel-15 allowances to make more optimal scheduling decisions.
  Vision is to target worst case 1 RB + 1 RB for improved A-MPR of [~5 dB] for a RIM3 in the -25 dBm/MHz region, 30 kHz SCS for NR
UEs supporting improved A-MPR allowances could signal better intra-band EN-DC performance via MPR versioning
  No requirement for actual hardware architecture, only compliance with improved allowances.
  UEs not compliant with improved A-MPR would not indicate support for this modified A-MPR and would support legacy A-MPR requirements

## Slide 3: Way Forward
Request UE vendors to provide information on actual and feasible antenna isolations for B41/n41 frequencies to validate improved antenna isolation assumptions.
Request component vendors to provide measurements of A-MPR requirements with new assumptions:
  Three values for antenna isolation of 20 dB, 16 dB, and 13 dB
  Post PA loss of 4 dB
  Power Class 2 Tx chains (LTE and NR)
  Equal Power on LTE and NR
  1RB + 1 RB allocations
    If results of 1 RB + 1RB appear promising, additional allocations, with equal allocation sizes, to align with existing curve inflections points
  Determine backoff required to meet -13, -25, and -30 dBm/MHz limits