## Slide 1: WF on SAR solution for SUL PC2 UE
CMCC
TSG-RAN Working Group 4 (Radio) meeting #91 R4-1907657
Reno, NV, USA, 13 – 17 May 2019

## Slide 2: Background
SAR issue for PC2 NUL+PC3 SUL band combination in FR1 was raised in R4-1904547.
For SUL band combination, the configured transmit power requirement for serving cell is applied for each UL carrier, which means that PC2 NUL+PC3 SUL is supported in Rel-15.
UE capability maxUplinkDutyCycle for FR1 PC2 is introduced in Rel-15. The default value is 50% (if UE does not report the capability).
For PC2 NUL+ PC3 SUL, If a UE transmits 50% of the time at 26 dBm and 50% of the time at 23 dBm both in FR1, the SAR level for SUL band combination could be 50% higher linearly than for the NUL band alone at 50% duty cycle.

## Slide 3: Agreement
In Rel-15, there will be no specification change in order to solve the SAR issue for PC2 NUL+ PC3 SUL.
  The SAR issue can be solved by UE implementation, e.g. P-MPR
In Rel-16, the standardized SAR solution will be studied.
  similar methodology for FDD+TDD ENDC HPUE can be considered to solve the SAR issue for PC2 NUL+ PC3 SUL.
  Other solutions are not precluded.

## Slide 4: Reference
[1] R4-1906872, SAR considerations for SA SUL band combinations
[2] R4-1905556, Discussion on SUL HPUE SAR solutions
[3] R4-1906876, Considerations for potential SAR issues with NR UL + SUL
[4] R4-1907058, SAR Proposal for SUL with NR PC2 band