## Slide 1: Way forward on IAB OTA Timing and RRM
Ericsson, Samsung, Nokia, Nokia Shanghai Bell, Huawei, HiSilicon
3GPP TSG-RAN WG4 Meeting # 91
Reno, USA, May 13-17, 2019
Agenda: 8.5.4
R4-1907732

## Slide 2: Background
IAB OTA Synchronization
  Existing timing advance (TA) mechanism (in Rel-15) is used for OTA time alignment of IAB node.
  An IAB node shall set its DL TX timing ahead of its DL Rx timing by TA/2 + T_delta
    T_delta is signalled by the parent IAB node. Where:
      T_delta = (TA_offset - Tg)/2 and TA = NTATc; according to [1].
      T_delta = - Tg/2 and TA = (NTA + NTA_offset)Tc according to [2].
IAB RRM:
  IAB node has access and backhaul links (Section 7.3, TR 38.874 v16.0.0):
    Access link: link between an access UE and an IAB-node or IAB-donor.
    Backhaul: link between an IAB-node and an IAB child node or an IAB parent node.
  IAB node does not support mobility.
References:
  [1] R1-1903810/R4-1902804, LS on OTA timing alignment for IAB, RAN1 LS to RAN4
  [2] R4-1905306/R1-1905842, LS on clarification of OTA timing alignment for IAB, RAN1 LS to RAN4

## Slide 3: Way Forward on OTA Time Alignment
Range and granularity of T_delta:
  At least the following factors need to be considered for deciding the range and granularity of T_delta:
  Errors associated with the existing TA mechanism (in Rel-15):
    Bias in NTA.
    TA command resolution.
  The granularity of T_delta shall be finer than the granularity of TA command.
IAB OTA synchronization:
  Option 1: Do not specify OTA synchronization (OTA-S) accuracy for IAB node.
  Option 2: Specify OTA-S accuracy for IAB node.
  Factors impacting OTA-S accuracy need to be considered for deciding one of the options.

## Slide 4: Way Forward on IAB RRM
Access Link (AL):
  A UE served by an IAB node on the access link (Uu) shall meet existing RRM requirements for the access link (Uu) defined in 38.133 and 36.133 (related to EN-DC or NE-DC).
    No additional requirements related to UE operation on the access link are needed.
Backhaul link (BL):
  It is FFS whether any RRM requirement need to be specified for IAB node and identify type of RRM requirement(s) (if need to be specified).