## Slide 1: Way forward on antenna gain and minimum applied Noc for FR2 testing
Ericsson
3GPP TSG-RAN WG4 Meeting #91
Reno, NV, USA, 13 – 17 May, 2019
R4-1907736

## Slide 2: Background
  According to SS-RSRP definition in 38.215, FR2 measurement is performed on the combined signal from antenna elements
    For frequency range 2, SS-RSRP shall be measured based on the combined signal from antenna elements corresponding to a given receiver branch
  The reported SS-RSRP is therefore expected to depend on antenna/ beamforming gain and UE calibration. A device with higher antenna/ beamforming will report a higher SS-RSRP and vice versa
  The experienced/reported SS-RSRP is necessary for at least the following purposes
    Enabling absolute accuracy of UE measurement reports to be verified
    Correctly configuring event triggering thresholds in RRM tests
    Absolute thresholds in reselection test cases
  The following proposals for antenna gain were discussed in RAN4#91
Rough beam antenna gain range | Ericsson | Huawei
 | PC3 | PC3
Maximum | 17 dBi | 17 dBi
Minimum | 7-YdBi (beam peak); -5-ZdBi (non-beam peak) | -7 dBi

## Slide 3: Background : Tentative agreement on antenna gain in RAN4#91
  Rough beam antenna gain range for PC3
    Maximum
      Option 1: [17] dBi
      Option 2: not define
    Minimum
      [-7]dBi for beam peak
      FFS for non-beam peak

## Slide 4: Way forward
Investigate feasibility and value of upper bound for reported SS-RSRP value
  Whether upper bound should be specified, including
    Limitation on allowable UE implementations
    Whether tests remain meaningful if maximum SS-RSRP is unbounded
    Nominal RSRP in UE calibration
  If feasible, the suitable value for the upper bound.
Investigate suitable lower bound for reported SS-RSRP value for AoA setup 1 and AoA setup 2,3
  Analysis may consider reference sensitivity, agreed Y & Z values, and the definition of array gain used in the derivation of Y1, Y2, Y3, Y4 & Z1, Z2, Z3 and Z4.
  Nominal RSRP in UE calibration
Investigate how to capture the outcome in TS38.133
  Option 1 : Capture suitable event triggered reporting thresholds in tests, and minimum / maximum expected L1/L3 SS-RSRP in absolute accuracy testing
  Option 2 : Capture in a general section in annex A
  Option 3 : Capture in section 10
  Option 4 : Other option is not precluded

## Slide 5: Way forward(2)
Investigate feasibility and value of upper bound for antenna gain including
  Whether upper bound should be specified, including
    Limitation on allowable UE implementations
    Whether tests remain meaningful if maximum SS-RSRP is unbounded
  If feasible, the suitable value for the upper bound eg confirm if square brackets can be removed from the tentative agreement
Investigate suitable lower bound for antenna gain for OTA setup 1 and OTA setup 2,3
  Analysis may consider reference sensitivity, agreed Y & Z values, and the definition of array gain used in the derivation of Y&Z
Investigate how to capture the outcome in TS38.133
  Option 1 : Capture suitable event triggered reporting thresholds in tests, and minimum / maximum expected SS-RSRP in absolute accuracy testing
  Option 2 : Capture in a general section in annex A
  Option 3 : Other option is not precluded

## Slide 6: Background – Applied Noc
It has been agreed that in the SS-RSRP accuracy test
  Define SS-RSRP test with low input signal level
  No external noise is added
For higher level SS-RSRP accuracy test and all other tests, a noise signal (Noc) shall be applied
The Noc level needs to be sufficiently high that it can be used to control SNR, and the residual impact of the UE self noise should be minimimal at the chosen test point
Assuming noise powers can be added in the power domain and a worst case noise floor based on agreed side conditions, the residual impact may be evaluated as shown on the next slide

## Slide 7: Background – residual impact of UE self noise (worst case)
Chart: Worst case residual impact of UE self noise

## Slide 8: Way forward
Test cases where noise is added shall by default use Noc ≥6dB above the assumed UE noise floor
This gives a worst case residual impact of UE self noise at baseband of 1dB
To allow for this, 1dB margin shall be allowed in the lowest Es/Iot tested with respect to the Es/Iot side condition
  Eg if the side condition is Es/Iot≥-6dB, the test should target -5dB as lowest applied Es/Iot at reference point
The assumed UE noise floor may be found from applicable side condition (Minimum SSB_RP) already specified in annex B.2 by
UE assumed noise floor in dBm/120kHz=Minimium SSB_RP-ΔRRM,sc
  ΔRRM,sc = -6dB if intra minimum SSB_RP is used, or equivalently -4dB if inter minimum SSB_RP is used will give same value
Maximum Io RRM side condition of -50dBm for measurement also needs to be met in all tests

## Slide 9: Example for PC3, n260, ΣMBP=0, testing in non peak beam direction
UE assumed noise floor = -103.9dBm/120kHz+Z3+6dB
Using agreed Z3=7dB, UE assumed noise floor =-90.9dBm/120kHz
Conclusions for this example under the WF:
  Minimum Noc that can be used in tests is 6dB above UE assumed noise floor= -84.9dBm/120kHz
  Minimum Es/Iot that can be used in tests at reference point = -5dB to account for possible residual impact of UE own noise
Note that this Noc by itself already gives Io=-55dBm/95.04MHz, so testing is not feasible with significant positive Es/Iot for any cell with the current side condition for Io/channel BW≤-50dBm

## Slide 10: Issues for further study
Whether Noc level is agnostic to band and UE Power class
  Option 1: define based on worst case (currently PC3, n260)
  Option 2: define a different Noc for each band -> impacts all other power levels in the test
How to reflect ΣMBP in Noc setting
  Option 1: Assume worst case ΣMBP from 38.101-2 -> further limits dynamic range available in tests and may change in future releases
  Option 2: Paramerised tests using actual ΣMBP -> impacts all other power levels in the test
Whether setting Noc 6dB above UE noise can be used in all test cases
  Depending on whether all applicable side conditions can be met with default Noc setting