## Slide 1: WF on BS PA and filter aspects for 7 – 24 GHz range
Huawei, Ericsson
3GPP TSG-RAN WG4 Meeting RAN4#91 R4-1907794
Reno, USA, 13th – 17th May, 2019

## Slide 2: Background
The following papers on PA technology were considered in RAN4#91:
PA
  R4-1906787 PA characteristic for 7-24GHz ZTE
  R4-1906184 Elaboration on 7-24 GHz PA power scaling and AAS dependency Ericsson
  R4-1906180 Further elaboration on 7-24 GHz PA dependencies for different example frequencies Ericsson
  R4-1906884 BS RF technology aspects for 7-24 GHz Nokia
  R4-1906183 TP to TR 38.820: Addition of PA parameter dependency for different example frequencies in sublcause 6.3 Ericsson
  R4-1906168 TP to TR 38.820: Addition of power scaling and AAS dependency approaches in sub-clause 6.3 Ericsson
Filters
  R4-1906076, further elaboration on 7-24 GHz filtering , Ericsson
  R4-1906843, On performance of RF filters for 12GHz range, LGE
  R4-1906884, BS RF technology aspects for 7-24 GHz , Nokia

## Slide 3: Discussion Summary
The ad hoc discussion focused on:
Power and ACLR capability trends over frequency
  Focused on PA devices
  Relationships derived based on fixing certain parameters (such as PAE)
Dependence on transmitter architecture
  Importance (or not) of beam forming method (digital or hybrid)
  Impact of linearization (e.g. DPD) on PA performance
    Frequency dependency
    BW dependency
Frequency dependent technology break point.

## Slide 4: WF on Architecture
Discussion
  It seems that there is a technology break point at approx. [10 to 13GHz]. This breakpoint effects:
    PA device technology and max power capability
    Linearization feasibility
    beam forming architecture (digital, hybrid, etc…)
  Below the breakpoint we assume:
    Linearization is feasible so system performance is not totally reliant on PA device performance
  Above the breakpoint we assume
    System performance is directly related to PA device performance
WF
  Provide contributions on how architectural issues affect the PA analysis and the BS specifications.
  Provide further views on potential frequency break point and approx. value of it (other components may effect break point, this is specifically for PA).

## Slide 5: WF on PA Device performance
Discussion
  Information discussed so far consists of:
    Papers capture published PA data and analysis
    Trends vs frequency are identified by fixing some parameters (ACLR, PAE, P_out) and investigating others.
WF
  Identify how to capture such informative data whilst maintaining suitable caveats about the fixed parameters and assumptions.
  Study other parameters e.g. EVM

## Slide 6: WF on filters
Discussion
  The LGE results for LTCC at 15GHz seemed to provide higher Q than the Ericsson results at 20MHz
  The manufacturing tolerances need to be checked / confirmed
  Other types of filter, such as ceramic may be considered, in particular for lower frequencies
WF:
  Provide data on expected LTCC performance at other example frequencies and attenuation levels
  Provide further analysis of factors impacting LTCC Q
  Provide data on expected PCB mounted performance at other example frequencies and attenuation levels
  Provide inputs on possibilities with other filter types