## Slide 1
3GPP TSG-RAN WG4 Meeting #91
Reno, Nevada, U.S., 13th – 17th May, 2019
Agenda item: 8.4.2
Document for : Approval
LG Electronics
WF on Coexistence Scenarios
and Simulation Parameters
R4-1907821

## Slide 2: Background (1)
In device coexistence
  (LTE SL and NR SL operation at ITS spectrum) without (LTE or NR Uu in another band) on the same device
    TDM operation in 5.9 GHz ITS spectrum.
      Based on approved WID, no self interference issues are identified for the IDC
        Switching times for TDM operation needs to be studied
    FDM operation
      The inter-band FDM operation includes a band for LTE SL (at 5.9GHz) and a band for NR sidelink operation. RAN4 defers the coexistence discussion to May meeting. Some feedback from 5GAA and operator expected. Final decision on band is discussed in RAN4.
  * There is no self interference problem in ITS spectrum
In-device Inter-band con-current operation
  (LTE SL and NR SL operation at ITS spectrum) with (LTE or NR Uu in another band) on the same device
    Both TDM/FDM operation will be studied based on operator request
    RAN4 defers the coexistence discussion to May meeting. Final decision on band combinations are discussed in RAN4.

## Slide 3: Background (2)
UE-to-UE coexistence
  1) 5.9 GHz ITS spectrum
    Aggressor-to-Victim UE coexistence
      NR SL-to-DSRC, NR SL-to-LTE SL
      DSRC-to-NR SL, LTE SL-to-NR SL
    In LTE SL WI, RAN4 already analyze the DSRC impact
    For the new unlicensed ITS spectrum, RAN4 will discuss when it is available
  2) Licensed spectrum
    Aggressor-to-Victim UE coexistence
      NR SL-to-NR/LTE Uu
      LTE/NR Uu-to-NR SL
    RAN4 need to UE-to-UE coexistence parameters and assumptions for these scenarios.
    However, RAN4 defer the coexistence discussion at May meeting. Some feedback from 5GAA and operator expected. Final decision on bands are discussed in RAN4.

## Slide 4: Coexistence Scenarios in ITS Spectrum
  ITS spectrum(5.9GHz)
    Case1: NR V2X UE-to-DSRC UE (REF : DSRC UE-to-DSRC UE)
    Case2: DSRC UE-to-NR V2X UE (REF : DSRC UE-to-DSRC UE)
    Case3: NR V2X UE-to-LTE V2X UE (REF: LTE V2X UE-to-LTE V2X UE)
    Case4: LTE V2X UE-to-NR V2X UE (REF: LTE V2X UE-to-LTE V2X UE)
  Deployment simulation parameters based on TR36.785 (LTE V2X WI) in RAN4 & TR37.885(NR V2X WI) in RAN1

## Slide 5: Coexistence Scenarios in ITS Spectrum
Case 1 (Aggressor-Victim)
  NR V2X UE-to-DSRC UE
Case 2 (Aggressor-Victim)
  DSRC UE-to-NR V2X UE
Case 3 (Aggressor-Victim)
  NR V2X UE-to-LTE V2X UE
Case 4 (Aggressor-Victim)
  LTE V2X UE-to-NR V2X UE
  Consider NR/LTE V2X SL operation in 5.9GHz
    No LBT mechanism for LTE V2X UE and NR V2X UE
    Max. output power for DSRC, NR V2X and LTE V2X UE are either 23dBm or 33dBm
DSRC
NR V2X
f
LTE V2X
NR V2X
f
NR V2X
DSRC
f
NR V2X
LTE V2X
f

## Slide 6: Coexistence Scenarios in FR1
  Licensed spectrum(2GHz FDD, 3.5GHz TDD)
    Case5: NR V2X UE-to-NR Uu BS (REF: NR UE-to-NR BS)
    Case6: NR Uu UE-to-NR V2X UE (REF: victim PRR without aggressor)
    Case7: NR V2X UE-to-LTE Uu BS (REF : LTE UE-to-LTE UE)
    Case8: LTE Uu UE-to-NR V2X UE (REF: victim PRR without aggressor)
  Deployment simulation parameters based on TR37.885(NR V2X) in RAN1 and TR36.942(LTE/NR Uu) in RAN4

## Slide 7: Coexistence Scenarios in FR1 Licensed spectrum
Case 5 (Aggressor-Victim)
  NR V2X UE-to-NR Uu BS
Case 6 (Aggressor-Victim)
  NR Uu UE-to-NR V2X UE
Case 7 (Aggressor-Victim)
  NR V2X UE-to-LTE Uu BS
Case 8 (Aggressor-Victim)
  LTE Uu UE-to-NR V2X UE
  Consider LTE-based V2X operation at 2GHz and 3.5GHz
    No LBT mechanism for LTE V2X UE & NR V2X UE
    Max. output power for NR/LTE UE are either 23dBm(FDD) or 23dBm/26dBm(TDD)
NR Uu
NR V2X
f
LTE Uu
NR V2X
f
NR V2X
NR Uu
f
NR V2X
LTE Uu
f

## Slide 8: Coexistence Scenarios in FR2
  Licensed spectrum(28GHz TDD)
    Case9: NR V2X UE-to-NR Uu BS (REF : NR Uu UE-to-NR Uu BS)
    Case10: NR Uu UE-to-NR V2X UE (REF: victim PRR without aggressor)
  Deployment simulation parameters based on NR V2X TR37.885 in RAN1 and TR38.803 for NR Uu in RAN4
    If interested companies provide the simulation results, RAN4 can make conclusion in FR2 coexistence.
  FR2 will be treated as 2nd priority

## Slide 9: Coexistence Scenarios in FR2 Licensed spectrum
Case 9 (Aggressor-Victim)
  NR V2X UE-to-NR Uu BS
Case 10 (Aggressor-Victim)
  NR Uu UE-to-NR V2X UE
  Consider NR V2X parameters in 28GHz in TS37.885
    No LBT mechanism for NR V2X UE
    Min. peak EIRP for NR UE : PC3 for handheld UE
    Min. peak EIRP for NR V2X UE: PC2 for vehicular UE
    Beamforming of NR V2X UE is depend on interested companies’ view
NR Uu
NR V2X
f
NR V2X
NR Uu
f

## Slide 10: General Simulation Paramters
Only outdoor deployment will be considered
Deployment scenarios: Urban grid in Annex I, Highway (optional)
Simulation Block Size :
  Urban : Manhattan grid model: 3*433m, 3*250m
Absolute vehicle speed for urban
  Urban : 15km/h, 60km/h
    Used only to decide vehicle density
    Follow TR36.885 for LTE V2X and TR37.885 for NR V2X
  Fixed location will be considered for adjacent channel coexistence evaluation
  All vehicle UE has both LTE V2X and NR V2X,
    The Tx between LTE V2X and NR V2X is TDM, while Rx between LTE V2X and NR V2X is simultaneous.
Traffic model:
  Dependent on UE velocity (LTE ref.:36.785, NR ref.: TR37.885)
    For the NR traffic, medium intensity aperiodic traffic model will be used.
    LTE traffic model
      Option1: UE activation rate: 1%
      Option2: 15km : 0.1% or 60km: 0.33%
RAN1 dependent parameter
  Power control scheme, RAN4 can revisit the PC according to RAN1 decision, but following is initial
    In licensed spectrum, OLPC in TR36.786 is used
    In ITS spectrum, worst case of no power control is used
  For licensed band, NR SL operation in Uplink band in FDD, UL opportunity in TDD is considered.

## Slide 11: Simulation Parameters Specific to ITS
Pathloss models
  NR V2X UE-to-DSRC UE : Follow TR 37.885
  NR V2X UE-to-LTE UE : Follow TR 37.885
ACLR and ACS for DSRC UE (10MHz)
  UE ACLR= 38 dB
  UE ACS = 22/25/29dB.
ACLR and ACS for LTE V2X UE (20MHz)
  UE ACLR= 30 dB
  UE ACS = 27dB
Tentative ACLR and ACS for NR V2X UE (40MHz)
  For 23dBm V2X UE, UE ACLR =30/33dB, UE ACS= 33/37dB
  For 33dBm V2X UE, UE ACLR =31/34dB, UE ACS= 33/37dB

## Slide 12: Simulation Parameters Specific to Licensed FR1
Pathloss models
  NR/LTE Uu UE-to-NR/LTE BS: Table 5.4.2.1-1 in TR37.885
  NR/LTE Uu UE-to-NR V2X UE: Table 5.4.3.1-1 in TR37.885
Used ACLR and ACS for legacy LTE & NR BS/UE (20MHz)
  BS ACLR=45dB, BS ACS=46dB
  LTE/NR UE ACLR=30dB, LTE/NR UE ACS=27dB
Tentative NR V2X UE ACLR and ACS (40MHz)
  Consider same RFIC and PA in licensed band
    V2X UE ACLR=30dB, V2X UE ACS=24dB (FDD at 2GHz), 33dB (TDD at 3.5GHz)

## Slide 13: Simulation Parameters Specific to Licensed FR2
Pathloss models
  NR V2X UE-to-NR gNB : Follow TR 37.885
  NR Uu UE-to-NR V2X UE: Follow TR37.885 (P2V model)
Used ACLR and ACS for legacy NR gNB/UE (200MHz)
  gNB ACLR=28dB, gNB ACS=23.5dB
  NR UE ACLR=17dB, NR UE ACS=23dB
Tentative NR V2X UE ACLR and ACS (200MHz)
  Consider same RFIC and PA in licensed band
    NR V2X UE ACLR=17dB, NR V2X UE ACS=23dB

## Slide 14: Evaluation Methodology
Static simulations
  Monte-carlo based static system simulations.
Evaluation metric
  PRR degradation due to adjacent channel interferer(s) for both DSRC and NR/LTE V2X system in 5.9GHz
  Legacy system throughput degradation due to adjacent channel interferer(s) in both licensed FR1 and FR2 spectrum
  Link level simulation mapping model for LTE V2X UE is referred in Annex A in TR36.785
    It will be updated at 2GHz/3.5GHz and 28GHz for NR V2X UE. Detail simulation parameters are FFS.

## Slide 15: Way Forward
Coexistence scenarios in pages 4 to 9 will be used
Coexistence parameters in pages 10~13 will be used
Evaluation methodology in page 14 will be used
If there are scenarios with no input from company by RAN4#92bis, these will be discarded in Rel-16.

## Slide 16: Annex I: Parameters for urban deployment
ISD of gNB = 500m at FR1
ISD of gNB = 200m at FR2, detail deployment parameters will be proposed in e-mail reflector
  # of LTE/NR UE is 20 per macro cell
  UEs are dropped with the equal inter-UE distance in the middle of the sidewalk

## Slide 17: Annex II : Activated User Number
Number of activated V2V UEs per cell: round (1%* total # of dropped UEs/cell)
  E.g) 15km/h case: [(2676/10.4)*9]*0.01 = [257.3*9]*0.01 = 23 UEs
  E.g) 60km/h case: [(2676/41.7)*9]*0.01= [64.2*9]*0.01 = 6 UEs
    In here, 2676 = 433*4 +236*4