## Slide 1: 3GPP TSG-RAN WG4 Meeting #92 Ljubljana, SI, 26th – 30th August 2019
Qualcomm Incorporated, …
Performance Difference between Different SSB Locations in NR-U
R4-1910532

## Slide 2: SSB in Center of sub-band
RAN1 perspective:
  Non continuous RBs available to carry SIB1 in RMSI PDSCH:
    RMSI PDSCH cannot currently rate-match around SSB
      Rate matching behavior will have to be defined
      Other options (resource allocation with discontinuous RBs, smaller RMSI size) can also be explored but will have specification impact
  CSI-RS cannot be FDM’ed with SSB unless specification is modified (i.e., non-contiguous CSI-RS or CSI-RS rate matching)
    NOTE: RAN1 agreed CSI-RS can be transmitted together with SSB to fulfil OCB requirements.
    NOTE: Legacy CSI-RS (min of 24PRB) imply that RMSI can be transmitted only in 24 instead of 28PRBs. And specification change to R15 CSI-RS improves coverage/RMSI payload size.
  Forward compatibility
  Scell SSB can be OFF the synch raster, and rate-matching of RMSI may be anyway needed for essential (RMSI (PLMN) transmission in Scell) case

## Slide 3: SSB in Center of sub-band
RAN4 perspective:
  Similar impact of adjacent channel interference on SSS detection performance when the SSB is placed at the edge of sub-band or in the center of sub-band: less than 1% SSB detection performance gain could be observed in simulation results when SSB is placed in the center.
  Common sync raster point can be defined at least for 20, 40, 80 MHz carriers, further reducing total number of SSB raster points the UE needs to search considering different carrier bandwidths
  When utilizing in wideband operation, changes in the size of inter-carrier guardbands and/or number of intra-carrier guard PRBs due to e.g. different NS signaling will most likely not change the location of the SSB. This improves forward combability if scheduling in the intra-carrier guard PRBs is introduced and if the same approach for placement of SSB are to be reused for 6GHz deployment.
Proponents: Nokia, Huawei, OPPO

## Slide 4: SSB in Edge of sub-band
RAN1 perspective:
  Continuous RBs available to carry SIB1 in RMSI PDSCH:
    RMSI PDSCH rate-matching around SSB may not be needed for typical SIB1 payloads
    Scell SSB can be OFF the synch raster, and rate-matching of RMSI may be anyway needed for essential (RMSI (PLMN) trasmission in Scell) case
  CSI-RS can be FDM’ed with SSB without specification impact
    NOTE: RAN1 agreed CSI-RS can be transmitted together with SSB to fulfil OCB requirements.
    NOTE: Legacy CSI-RS (min of 24PRB) imply that RMSI can be transmitted only in 24 instead of 28PRBs. And specification change to CSI-RS improves coverage/RMSI payload size.

## Slide 5: SSB in Edge of sub-band
RAN4 perspective:
  Similar impact of adjacent channel interference on SSS detection performance when the SSB is placed at the edge of sub-band or in the center of sub-band: less than 1% SSB detection performance loss could be observed in simulation results when SSB is placed in edge
  Common sync raster point can be defined at least for 20, 40, 80 MHz carriers, further reducing total number of SSB raster points the UE needs to search considering different carrier bandwidths
  When utilizing in wideband operation, changes in the size of inter-carrier guardbands and/or number of intra-carrier guard PRBs due to e.g. different NS signaling will most likely not change the location of the SSB because SSB raster position is fixed (UE hardcoded ARFCN at initial access)
  LS from RAN1 suggests SSB close to edge, not exactly aligned with the edge.
  Proponents: Qualcomm Incorporated, Ericsson, MediaTek, Charter Communications, AT&T

## Slide 6: LS quote from RAN1 [R4-1907801]
From a RAN1 perspective, in unlicensed bands, where the DL initial BWP is nominally 20 MHz, RAN4 decisions on sync raster points have consequences on RAN1 design. RAN1 has discussed these consequences.
  If a SSB is not close to the edge, the number of RBs available to carry SIB1 would be limited although further enhancement to introduce rate matching around the SSBs to address this limitation are being discussed in RAN1
  If a SSB is close to the edge, the number of RBs available to carry SIB1 would be less limited although whether or not further enhancement to introduce rate matching around the SSBs is needed is being discussed in RAN1