## Slide 1: WF on NR V2X RRM requirement
LG Electronics, MediaTek
3GPP TSG-RAN WG4 #92bis Meeting
Chongqing, China, 14th – 18th Oct, 2019
R4-1912708

## Slide 2
RRM requirements shall be specified based on NR SL in FR1 ITS band
Scenario for RRM requirements

## Slide 3
For SyncRef UE identification & S-RSRP
  Propagation Condition
    AWGN
    Fading
      TDLC-30ns-1400Hz
      TDLC-100ns-300Hz
      TDLC-10ns-1400Hz
      TDLC-100ns-150Hz
  SLSS ID Combinations(other options are not precluded)
  The conclusion of RAN1 SLSS design based on the LS to RAN1 discussed in RF room will be taken into consideration when defining synchronization requirement
Simulation Assumption
Case # | SyncRef UE 1 | SyncRef UE 2
1 | 336+112 | 112
2 | 336+224 | 112

## Slide 4
UE Tx Timing
FFS whether gNB in FR2 is considered as timing reference source or not
  If considered, use the values which were addressed in RAN4#92(excel sheet in R4-190993)
  If not considered, do not specify

## Slide 5
With current RAN1 agreement on synchronization source priority, in following scenarios timing misalignment may exist between UEs communicating on SL
  UE1 and UE2 synced to two different gNBs, but the 2 gNBs are with different timing
  UE1 and UE2 synced to two different eNBs, but the 2 eNBs are with different timing
  UE1 synced to eNB, UE2 synced to gNB, eNB and gNB are with different timing
RAN4 sends LS to ask RAN2 to check if there is any signalling available for timing adjustment in the above scenarios where multiple gNB/eNB with different timing are presented
Synchronization(1/4)

## Slide 6
Potential issue for initiation/cease of SLSS Tx
  RAN4 should study the following scenario:
    In EN-DC/NE-DC,
      Sidelink UE will possibly experience Ping-Pong effect when reselecting the sync. reference source since gNB & eNB are in the same priority
      Therefore, sidelink UE may suffer Ping-Pong effect between transmitting or not transmitting SLSS Tx if Pcell and PSCell have the different RSRP.
Synchronization(2/4)

## Slide 7
UE capable number of intra-frequency V2X SyncRef UE performing S-RSRP measurements
  [3] same as LTE-V2X
Dropping Rate for selection/reselection of NR V2X synchronization reference source
  Define it by at least considering NR SyncRef UE search and PBCH reading time
  The side condition should be [0]dB
  Study Rx dropping requirement by considering NR SyncRef UE identification performance and UE implementation constraint
  Tx dropping requirement
    Option 1: following LTE, dropping SLSS Tx and data Tx for 3 SLSS period in asynchronized case, dropping SLSS Tx for 3 SLSS period in synchronized case
    Other options are not precluded
Synchronization(3/4)

## Slide 8
Evaluation time for initiation/cease SLSS Tx
  gNB as synchronization source
    FFS evaluation time
    Related measurement time follows NR intra-frequency measurement requirement
  eNB as synchronization source
    Reuse LTE-V2X requirement
  GNSS as synchronization source
    Depending on RAN1 decision
  SyncRef UE as synchronization source
    To be defined based on the measurement simulation in next meeting
Synchronization(4/4)

## Slide 9
SSB RSRP measurement
  Simulation assumption
    follow synchronization simulation assumptions
  Measurement accuracy
    reuse the same accuracy from NR Uu , side condition pending simulation results
  Measurement period
    Pending simulation results
Autonomous Resource Reselection measurement
  Evaluate only L1 SL-RSRP measurement for autonomous resource selection/reselection. For it, RAN4 need to wait RAN1 agreement for RS design related L1 SL-RSRP
Congestion Control measurement
  Pending RAN1 discussion for whether to use S-RSSI based congestion control
Measurement

## Slide 10
Only focus on PC5 to Uu interruption
Interruption

## Slide 11
Baseline of Spec. Skeleton
  - 12 V2X Requirements
    12.1 Introduction
    12.2 UE Transmit Timing
    - 12.2.1 Introduction
    - 12.2.2 GNSS as synchronization reference source
    - 12.2.3 NR cell as synchronization reference source
    - 12.2.4 E-UTRA cell as synchronization reference source
    - 12.2.5 SyncRef UE as synchronization reference source
    12.3 Initiation/Cease of SLSS Transmissions
      - 12.3.1 Introduction
      - 12.3.2 Initiation/Cease of SLSS Transmissions with NR cell as synchronization reference source
      - 12.3.3 Initiation/Cease of SLSS Transmissions with E-UTRA cell as synchronization reference source
      - 12.3.4 Initiation/Cease of SLSS Transmissions with GNSS as synchronization reference source
      - 12.3.5 Initiation/Cease of SLSS Transmissions with SyncRef UE as synchronization reference source
    12.4 Selection/Reselction of V2X Synchronization Reference Source
    12.5 [Autonomous Resource Selection/Reselection measurements]
      - 12.5.1 Introduction
      - 12.5.2 SL-RSRP measurements
    12.6 [Congestion Control measurements]
    12.7 Interruption
      - 12.7.1 [Interruption to WAN Communication due to V2X Sidelink]
      - 12.7.1.1 Introduction
      - 12.7.1.2 Requirements
    12.8 [Reliability of GNSS signal]
Spec. Skeleton