## Slide 1: 3GPP TSG-RAN WG4 Meeting #92bis Chongqing, China, October 14 -18, 2019
Ericsson, Huawei, HiSilicon, Qualcomm Incorporated, Nokia, Nokia Shanghai Bell
Way forward on Rel-16 MTC RRM enhancement
R4-1912735

## Slide 2: Wake-up signal
Based on the Rel-16 WUS contributions provided to RAN4#92bis meeting, following options are possible:
  Option 1: : Rel-15 WUS reception requirements apply for Rel-16 UE.
  Option 2: Required number of repetitions for WUS reception with 1 tx antenna when DRX cycle length is ≤ 1.28 s is increased from 32 to 64. Others can be kept unchanged.
Companies are expected to further study the WUS detection performance of each WUS sequence assuming UE monitors two sequences based on Rel-15 WUS framework in R4-1816334
RAN4 shall reach agreement at RAN4#93 meeting.

## Slide 3: Preconfigured UL resource
The first and the second measurement conditions agreed at RAN4#92 meeting (R4-1910107) include parameters M and N, whose values are defined as follows:
  When TA is obtained in RRC_CONNECTED mode: M=[TEvaluate_Qin_CatM1/2]
  When TA is obtained in RRC_IDLE mode:
    Option 1:
      M = min (Tmeasure_intra_UE cat M1 in nonDRX, DRX_cycle length)
      N = min (Tmeasure_intra_UE cat M1 in nonDRX, DRX_cycle length)
    Other options are not precluded.

## Slide 4: MPDCCH performance improvement for RLM
The evaluation period of DL radio link quality measurement is same as evaluation period for Rel-13 eMTC

## Slide 5: Mobility enhancement: RSS based RSRP measurement for BL CE UE
Es/Iot [dB] | Nokia | Ericsson | Huawei | Intel
≥ -6 | TBD | TBD | TBD | TBD
≥ -12 dB | TBD | TBD | TBD | TBD
-15 <= Es/Iot <= -12 dB | TBD | TBD | TBD | TBD
Delta RSRP = (estimated RSRP – ideal RSRP)
  Ideal RSRP: The ideal RSRP is the true value that does not include any channel estimation noise, i.e. it is taken at antenna connector of the UE and averaged over L1 measurement period.
  Estimated value = averaged over the samples within L1 measurement period.
Number of samples: 3 and 5
Companies are encouraged to provide simulation results for colliding and non-colliding RSS for relative power offset of 0 dB of neighbour cell against serving cell.
Accuracy levels are including the RF margin and companies are requested to present their assumption on RF margin.

## Slide 6: Mobility enhancement: RSS based RSRP measurement for non-BL CE UE
Delta RSRP = (estimated RSRP – ideal RSRP)
  Ideal RSRP: The ideal RSRP is the true value that does not include any channel estimation noise, i.e. it is taken at antenna connector of the UE and averaged over L1 measurement period.
  Estimated value = averaged over the samples within L1 measurement period.
Number of samples: 3 and 5
Companies are encouraged to provide simulation results for colliding and non-colliding RSS for relative power offset of 0 dB of neighbour cell against serving cell.
Accuracy levels are including the RF margin and companies are requested to present their assumption on RF margin.
Es/Iot [dB] | Nokia | Ericsson | Huawei | Intel
≥ -6 | TBD | TBD | TBD | TBD
≥ -12 dB | TBD | TBD | TBD | TBD
-15 <= Es/Iot <= -12 dB | TBD | TBD | TBD | TBD

## Slide 7: DL quality reporting
Measurement period for DL quality reporting in idle mode is T2
RAN4 is to not discuss further on 8 bit table report mapping table.
MSG3 quality reporting in eMTC should have at least the same accuracy requirements as in NB-IoT since the operating region is similar

## Slide 8: DL quality reporting
Attribute | Normal coverage/CEModeA | Enhanced coverage/CEModeB
DCI format | 6-1A | 6-1B
Starting OFDM symbols | 2; Bandwidth >= 10MHz 3; 3MHz <= Bandwidth < 10MHz 4; Bandwidth = 1.4MHz | 
MPDCCH repetition level Note1 | 1 | n.a.
MPDCCH Aggregation level (ECCE) Note2 | 24 | 
M-PDCCH Transmission type | Distributed | 
NOTE 1: Not applicable if repetition number in DL quality information is larger than 1. NOTE 2: Not applicable if repetition number in DL quality information equals to 1. |  | 
MPDCCH parameters for DL quality reporting is as follows: