## Slide 1: WF on RRM measurement relaxation for Power Saving
CATT
3GPP TSG-RAN WG4 Meeting #93 R4-1913740
Reno, USA, 18 - 22 Nov 2019

## Slide 2: Background
  During the RAN2#107bis meeting, the following agreements were achieved:
  Network can configure the triggering criteria independently (i.e. either cell-edge or low mobility or both)
  Cell-edge criteria will not consider neighbour cell measurements
  During the RAN4#92bis meeting, the following options were considered for RRM measurement relaxation :
  Option1: RRM measurement relaxation by allowing measurements with longer intervals, and/or by reducing the number of carriers to be measured;
  Option2: RRM measurement relaxation of neighbour cell monitoring in LTE MTC/NB-IoT can be reused for defining the RRM requirements for UE power saving in NR
  Other option is not precluded.

## Slide 3: WF on RRM measurement relaxation
Option1 defined in [1] is proposed to define RRM measurement relaxation for UE power saving in NR
For intra-frequency measurement and inter-frequency measurement with equal or lower priority, the RRM measurement relaxation can be triggered when the measurement relaxation criteria are fulfilled
For inter-frequency measurement with higher priority, UE is not allowed to relax the RRM measurement requirement

## Slide 4: WF on RRM measurement relaxation
Increasing measurement interval can be considered for UE power saving in NR
  FFS on how to extend measurement interval
Reducing the number of carriers to be measured can be considered for UE power saving in NR
  If inter-frequency carriers are in the same FR2 band, UE is required to measured one of the inter-frequency carrier in that FR2 band
  Other method is not precluded
  FFS the impact on RAN4’s spec

## Slide 5: Reference
1. R4-1910948 WF on Power Saving RRM requirements CATT, Vivo