## Slide 1: WF on CSI-RS L3 RRM requirements
CATT
3GPP TSG-RAN WG4 Meeting #93 R4-1913749
Reno, USA, 18 - 22 Nov 2019

## Slide 2: WF on CSI-RS configuration for measurement requirement
CSI-RS configurations (bandwidth of CSI-RS and density of CSI-RS resource) used to define requirements
Define requirements at least for 1 set of configurations
  Option 1: 48PRBs and D = 1
  Option 2: 48PRBs and D = 3
FFS whether to define requirements for additional configurations
  48PRBs and D = 1
  48PRBs and D = 3
  96PRBs and D = 1
  96PRBs and D = 3

## Slide 3: WF on MO configuration
MO configuration
  Case 1: all CSI-RS resources in the same MO have the same center frequency, BW, SCS, CP type configured.
  Case 2: all CSI-RS resources in the same MO have the same center frequency, SCS, CP type configured. BW can be different.
RAN4 will study the RRM requirements at least for Case 1 MO configuration. FFS how to address Case 2.
Note: this does not exclude defining requirements for Case 2.

## Slide 4: WF on CSI-RS based intra-frequency and inter-frequency measurement definition
Case 1: CSI-RS resource of serving cell is available
  CSI-RS based intra-frequency measurement: a measurement is defined as a CSI-RS based intra-frequency measurement provided that:
    the SCS of CSI-RS on the serving cell and neighbor cell is the same
    the CP type of CSI-RS on serving cell and target cell is the same
      It is applied for SCS = 60KHz
    the center frequency, bandwidth and active BWP
      Option 1: the center frequency of CSI-RS on the serving cell and neighbor cell is the same, and
      Option 2: the bandwidth of the CSI-RS on the neighbor cell is within the active BWP of the UE, and
      Option 3: the bandwidth of CSI-RS on the target cell is the same as bandwidth of CSI-RS resources on the serving cell
      Any combination of options above
  Note 1: the RAN4 design shall not contradict RAN2 agreements on MO signalling
  Note 2: the definition of intra-frequency and inter-frequency measurement shall not impact RAN1’s agreement on the definition of the same MO
Case 2: CSI-RS resource of serving cell is not available
  Option 1: All MO are inter-frequency
  Option 2: No requirement is applied