## Slide 1: WF on NR V2X RRM requirement
LG Electronics
3GPP TSG-RAN WG4 #93 Meeting
Reno, US, 18th – 22nd Nov., 2019
R4-1915783

## Slide 2
Transmit Timing (Te)
  Do not define NR V2X SL RRM requirements for the scenarios with FR2 gNB as synchronization source in Rel-16
  Do not define NR V2X SL RRM requirements for the scenarios with NR FR2 Uu in Rel-16
SyncRef UE identification time
  SyncRef UE identification time is 3 SLSS periods
    S-RSRP measurement period is not included in SyncRef UE identification time and shall be considered as a part of test case definition for the total measurement time
Initiation/cease SLSS Tx with gNB as synchronization
  For measurement time, re-use NR intra-frequency measurement with/without gaps time when gNB is used as synchronization reference source
  Tevaluate,SLSS for the case w/o Gap
Agreement from on-line session(1/2)
DRX cycle | Tevaluate,SLSS
No DRX | max(2x200ms, ceil( 2x5 x Kp) x SMTC period)
DRX cycle≤ 320ms | max(2x200ms, ceil(1.5 x 2 x 5 x Kp) x max(SMTC period, DRX cycle))
DRX cycle>320ms | ceil( 7 x Kp ) x DRX cycle

## Slide 3
TX Dropping Rate for selection/reselection of NR V2X synchronization reference source
Agreement from on-line session(2/2)
When GNSS synchronization reference source is configured as the highest priority UE is synchronized to GNSS directly: UE shall not drop any V2X SLSS and data transmission for the purpose of selection/reselection to the SyncRef UE UE is synchronized to a SyncRef UE that is synchronized to GNSS directly or in-directly: UE shall be able to identify newly detectable intra-frequency V2X SyncRef UE within X1 sec. UE is allowed to drop a maximum of Y1% of its SLSS transmissions during X1 sec for the purpose of selection / reselection to the SyncRef UE In other cases: UE shall be able to identify newly detectable intra-frequency V2X SyncRef UE within X2 sec. UE is allowed to drop a maximum of Y2% of its V2X data and SLSS transmissions during X2 sec for the purpose of selection / reselection to the SyncRef UE When serving cell/PCell synchronization reference source is configured as the highest priority UE shall be able to identify newly detectable intra-frequency V2X SyncRef UE within X2 sec. UE is allowed to drop a maximum of Y2% of its V2X data and SLSS transmissions during X2 sec for the purpose of selection / reselection to the SyncRef UE Where X1 = 1.6 sec Y1% = 30% X2 = 8 sec Y2% = 6%

## Slide 4
Not applicable scenarios
  Single carrier in NR V2X SL + EN-DC/NE-DC/NR-DC/NR-CA/LTE-CA/LTE-DC in Uu
    NR V2X SL is dedicated to NR V2X SL and is not used for Uu link
Not Applicable scenario

## Slide 5
Ping-Pong effect when gNB & eNB are in the same priority (EN-DC/NE-DC)
  Not consider in Rel-16
Study Ping-Pong effect when gNB is timing reference source
RX Dropping Rate for selection/reselection of NR V2X synchronization reference source
  UE is allowed to drop up to X slots of its V2X data reception per PSBCH monitoring occasion and overall drop rate shall not exceed [0.3%] of its V2X data reception during Tdetect,SyncRef UE_V2X for the purpose of selection / reselection to the SyncRef UE
  Define X value in next meeting
Synchronization(1/2)

## Slide 6
Initiation/cease SLSS Tx with gNB as synchronization
  Tevaluate,SLSS for the case with Gap
Initiation/cease SLSS Tx with GNSS as synchronization
  Reuse the evaluation time of gNB when gNB is serving cell and UE is in-coverage of gNB
  Reuse the evaluation time of eNB when eNB is serving cell and UE is in-coverage of eNB
  [ ] will be put in RRM spec. before RAN1’s agreement on it
Initiation/cease SLSS Tx with SyncRef UE as synchronization
  Side condition
    Option 1 : -6dB same as NR Uu measurement(LTE-V2X measurement)
    Option 2 : 0dB
    Other options are not precluded
  Measurement time of S-RSRP
    320ms
  Tevaluate,SLSS
    640ms
Synchronization(2/2)
DRX cycle | Tevaluate,SLSS
No DRX | max(2x200ms, 2 x 5 x max(MGRP, SMTC period)) x CSSFintra
DRX cycle≤ 320ms | max(2x200ms, ceil(1.5x2x 5) x max(MGRP, SMTC period,DRX cycle)) x CSSFintra
DRX cycle>320ms | 7 x max(MGRP, DRX cycle) x CSSFintra

## Slide 7
Interruption when NR Uu BWP switching, and RRC configuration/reconfiguration for SL(if supported) are performed simultaneously
  Following NR Uu, do not consider compound actions involving RRC reconfiguration in RAN4 requirement for single carrier in Uu link
Interruption requirement on Uu due to NR SL BWP re-configuration
  Do not define the requirement
Interruption requirement on Uu due to SL Tx/Rx operation in ITS band
  Do not define the requirement
  Note : Data drop may be possible due to power sharing between SL & UL, it does not define interruption
Interruption requirement on Uu due to NR SL carrier switching during the RRC reconfiguration procedure (no BWP switching)
  It is not a valid scenario in Rel-16
Interruption to SL due to synchronization source change
  Allow interruption of 1ms on SL Tx and Rx during synchronization source change for all SCS in NR V2X
Interruption to SL due to Uu RRC configuration
  Do not specify the requirement
Interruption

## Slide 8
Autonomous Resource Reselection measurement
  Define requirement for resource selection/reselection measurement based on single-shot L1 SL-RSRP
  Whether to define other measurement requirements needs RAN1’s further inputs
RSSI measurement for congestion control
  Base line is that the S-RSSI measurement accuracy requirements in LTE V2X can be reused for defining SL-RSSI measurement accuracy requirements in NR V2X
  After RAN1 measurement procedure is completed, it should be reconsidered
Resource pre-emption mechanism
  Study whether define or not requirement to verify resource pre-emption mechanism
Measurement

## Slide 9
Tx-Rx distance-based HARQ feedback for groupcast
  Study to introduce the requirement for distance-based HARQ feedback option 1
  Next meeting, RAN4 should decide whether to introduce the requirement
Unicast, groupcast related