## Slide 1: 3GPP TSG-RAN WG4 Meeting #93 Reno, Nevada, US, Nov 18-22, 2019
Huawei, HiSilicon
Way forward on NR HST PUSCH demodulation requirements
R4-1915870

## Slide 2: Background
The following WFs were approved:
  R4-1910128 Way forward on NR HST BS demodulation requirements, RAN4#92
  R4-1912809 Way forward on NR HST PUSCH demodulation requirements, RAN4#92Bis

## Slide 3: PUSCH
Maximum Doppler shift
  Single tap HST 500km/h
    15kHz SCS : 1740Hz
    30kHz SCS: 3334Hz
Carrier frequency
  500km/h for 15kHz SCS : 1.8GHz (Band n3)
l0 for PUSCH mapping type A
  l0 = 2 (For simulation alignment)
    If no performance different between l0 = 2 and l0 = 3, define performance requirements based on l0 = 2
    l0 value for testing is based on BS declaration

## Slide 4: PUSCH
Antenna configuration:
  Tunnel scenario: 1x2, FFS 1x1
    Test setup for conducted test with 1x1 needs further discussion
    FFS on OTA test for 1x1
    Whether to introduce test for 1x1 needs to consider the testable SNR value
  Open space scenario: 1x2 and 1x8
    As per BS declaration, only one antenna configuration is selected for test
    Define conducted tests for both 1x2 and 1x8
    Define OTA tests for 1x2 only
MCS
  350km/h
    Open space scenario: MCS 2 and MCS 16
    Tunnel scenario: MCS 2 and MCS 16
  500km/h
    Open space scenario: MCS 2 and MCS 16
    Tunnel scenario: MCS 2, FFS on MCS 16
TDD configuration
  Reuse the existing TDD configurations for 15 kHz SCS and 30 kHz SCS as baseline, i.e.
    15 kHz SCS: 3D1S1U, S=10D:2G:2U
    30 kHz SCS: 7D1S2U, S=6D:4G:4U
Test applicability
  The BS performance requirements for HST scenario are optional
  Not define PUCCH performance requirements for HST

## Slide 5: Simulation assumption for PUSCH
Parameter | Value |  |  |  | 
 | v = 350km/h |  | v = 500km/h |  | 
Transform precoding | Disabled |  | Disabled |  | 
Number of Tx | 1 |  | 1 |  | 
Number of Rx | Tunnel: 2, FFS on 1 Open space: 2, 8 |  | Tunnel: 2, FFS on 1 Open space: 2, 8 |  | 
Number of layers | 1 |  | 1 |  | 
SCS | 15kHz, 30kHz |  | 15kHz, 30kHz |  | 
Reference signal | DMRS type 1 with 1+1+1 |  | DMRS type 1 with 1+1+1 |  | 
l0 | l0 = 2 (for simulation alignment) (Note 1) |  | l0 = 2 (for simulation alignment) (Note 1) |  | 
symbols length | 14 |  | 14 |  | 
start symbol index | 0 |  | 0 |  | 
Time domain resource allocation type | type A |  | type A |  | 
Frequency domain resource | Full applicable test bandwidth |  | Full applicable test bandwidth |  | 
MCS index | Tunnel: MCS 2 and MCS 16 Open space: MCS 2 and MCS 16 |  | Tunnel: MCS 2, FFS on MCS 16 Open space: MCS 2 and MCS 16 |  | 
Maximum Doppler shift | 15kHz SCS: 1340Hz | 30kHz SCS: 2334Hz | 15kHz SCS: 1740Hz |  | 30kHz SCS: 3334Hz
Carrier frequency (GHz) | 15kHz SCS: 2.1GHz 30kHz SCS: 3.6GHz |  | 15kHz SCS: 1.8GHz (Band n3) 30kHz SCS: 3.6GHz |  | 
Propagation condition | HST single-tap channel model: Tunnel: Ds=300m, Dmin=2m Open space: Ds=700m, Dmin=150m |  |  |  | 
SCS and BW | 15kHz: 10MHz; 30kHz: 40MHz |  |  |  | 
Timing offset | 0 |  |  | 0 | 
Frequency offset | 0 |  |  | 0 | 
Code block group, Frequency hopping, Limited buffer rate matching | Disabled |  |  | Disabled | 
Number of HARQ transmissions | 4 |  |  | 4 | 
Testing metric | SNR @70% of maximum throughput |  |  | SNR @70% of maximum throughput | 
Note 1: Company is encouraged to evaluate the performance difference between l0 = 2 and l0 = 3 |  |  |  |  | 

## Slide 6: UL timing adjustment
Scenario for requirements
  Scenario Y
    A = 5us
    Δω = 0.26s – 1
  Note: Scenario X and Z also need to be scaled for 30kHz if Scenario X and Z are agreed after March discussion
SRS
  Transmit SRS (optional) for uplink timing advance requirement
    FDD:
      Transmit SRS in slot#1 in radio frames
    TDD:
      Transmit SRS in the last symbol in the special slot
        last symbol in slot #3 in radio frames for 15 KHz SCS, last symbol in slot #7 in radio frames for 30 KHz SCS
CBW&SCS
  10 MHz CBW / 15kHz SCS
  40MHz CBW / 30 kHz SCS
DMRS: 1+1+1

## Slide 7: UL timing adjustment
Allocated RBs for SRS
  10 MHz CBW / 15 kHz SCS: Single region with length of 40RBs
  40MHz CBW / 30 KHz SCS: Single region with length of 80 RBs
Allocated RBs for PUSCH
  10 MHz CBW / 15 kHz SCS: 25 continuously allocated RBs for each UE
    Starting PRB index for moving UE: 0
    Starting PRB index for stationary UE: 25
  40MHz CBW / 30 KHz SCS: 50 RBs continuously allocated for each UE
    Starting PRB index for moving UE: 0
    Starting PRB index for stationary UE: 50
PUSCH transmission
  FDD
    slot #0, #2, #4, #6, and #8 in radio frames
  TDD
    15 kHz SCS: slot #4 and #9 in radio frames
    30 kHz SCS: slot #8, #9, #18 and #19 in radio frames
Test metric
  Reuse LTE for performance requirement, maximum throughput for an FRC equals the Payload size* the Number of uplink subframes per second in which PUSCH is transmitted.

## Slide 8: UL timing adjustment
Antenna configuration:
  1x2
Waveform:
  CP-OFDM
PUSCH mapping type
  Type A and Type B
  l0 = 2
MCS for Scenario Y:
  MCS 16