## Slide 1: WF on FR2 DL Intra-band CA BW Enhancement
Qualcomm, Apple, Nokia, Samsung
­­­3GPP TSG-RAN WG4 Meeting #93 R4-1916021
Reno, NV, 18-22 Nov. 2019

## Slide 2: Background
Rel-16 DL CA BW enhancement feature is definition of DL-only frequency coverage spectrum [5]
Spectrum covered by Rel-15 DL frequency separation does not have the same properties as spectrum covered by Rel-16 DL-only spectrum
  They cannot be added into a single parameter
  Separate signaling must be introduced to describe properties of DL-only spectrum
  Any new signaling must be backward compatible with rel-15

## Slide 3: Way forward on signaling aspects
For Rel-16, extend the frequency separation class definition to include the following values for frequency separation ‘Fs’: {800, 1000, 1200, 1400, 1600, 1800, 2000, 2200, 2400} MHz
  Fs values > 1400 MHz apply to downlink frequency separation only
The signaling for DL-only frequency spectrum can be defined as below:
  Alt1: Introduce a new DL-only frequency separation class, ‘Fsd’, such that:
    A UE which has no restriction on the placement of UL coverage spectrum within the DL coverage spectrum does not signal this parameter
    A UE which needs to restrict the placement of UL coverage spectrum within the DL coverage spectrum signals Fs and also signals Fsd
    The following values for Fsd shall be used: {200, 400, 600, 800, 1000} MHz
  Alt2: Per RF chain reporting of Fs
The spectrum covered by the DL-only frequency separation shall be located relative to bidirectional spectrum(*) in one of two configurations:
  Extends on one side
  Extends equally on both sides, half on each side
    FFS if both-sided DL-only spectrum can be dropped for rel-16.
    Single bit can be used to indicate configuration if both possibilities retained
Total DL frequency Fs+Fsd <= 2400 MHz, where Fs >= Fsd
(*) Bidirectional spectrum is spectrum covered by DL frequency separation

## Slide 4: Reference contributions for RAN4#93
R4-1913140, ‘FR2 DL Intra-band CA BW Enhancement Feature Parameters’, Qualcomm
R4-1913538, ‘Views on FR2 frequency separation class enhancement’, Apple
R4-1914607, ‘Discussion on FR2 intra-band DL CA enhancement’, Nokia
R4-1915381, ‘On intra-band DL CA requirement for FR2’, Huawei
R4-1913042, ‘WF on DL Intra-band CA BW Enhancement’, Qualcomm