## Slide 1: WF for FR2 Intraband Non-contiguous UL CA MPR study
Nokia
R4-1916022

## Slide 2: Simulation/measurement assumptions
PA calibration point was 100 MHz, 120 kHz, QPSK, DFT-S-OFMA, 20RB23with 0 dB MPR
IQ-Image and LO leakage = 25 dBc
CIM3 = 60 dBc
Emission requirements as in 3GPP TR 38.831V0.1.0
Equal PSD
Equal backoff

## Slide 3: Simulation/measurement scenarios
2 sub-block and 3 sub-block configurations
UL Frequency separation up to 1400 MHz (Class III)
Allocation combinations should representative but not exhaustive

## Slide 4: MPR Schemes
MPR proposal shall include fallback to contiguous intra-CA MPR in case only one sub-block is configured for UL CA
In addition to modulation type, MPR can be function of allocation ratio ‘A’, other basis not precluded
  2CC example: A = (PRB1*SCS1 +PRB2*SCS2)/ (NRB1*SCS1 +NRB2*SCS2)