## Slide 1: WF on testing for NB-IoT operation in NR in-band
Nokia, Ericsson, Huawei, ZTE
3GPP TSG-RAN WG4 Meeting#93
Reno, Nevada, USA, 18 – 22 November 2019
Agenda Item: 8.11.2
R4-1916101

## Slide 2: Background
Way forward approved in RAN4#91:
R4-1907809, “WF on coexistence of NB-IoT with NR”, Huawei, HiSilicon, Ericsson, Nokia, ZTE, Dish, T-Mobile USA, CHTTL.
Contributions on testing for NB-IoT operation in NR in-band in RAN4#93:
[1] R4-1913796, “TP to TR 37.824: Update of MSR specification impact for NB-IoT operation within NR channel bandwidth”, Nokia, Nokia Shanghai Bell.
[2] R4-1913797, “Draft CR to TS 38.141-1: Introduction of NB-IoT operation in NR channel bandwidth”, Nokia, Nokia Shanghai Bell.
[3] R4-1914241, “Introduction of NB-IoT into TS37.141”, ZTE Corporation.

## Slide 3: Way forward on Capability Set Definition
Modify the existing MSR CS 16-19 to include optional support of NB-IoT operation in NR in-band.
  Support of E-UTRA remains mandatory in CS 16-19.
  No new CS need to be defined in TS 37.141.
BS that support NR with NB-IoT operation in NR in-band without the hosting E-UTRA shall be tested using TS 38.141-1.

## Slide 4: Way forward on Test Configuration Definition
Modify the existing MSR TC 21-22 in TS 37.141 to include optional support of NB-IoT operation in NR in-band.
Modify the existing TC or define new TC (depending on the resultant complexity and clarity) in TS 38.141-1 for testing BS that support NR with NB-IoT operation in NR in-band.
Only 15 kHz SCS is used in the TC for NB-IoT operation in NR in-band.
  Mixed numerologies between NR and NB-IoT has been agreed to be handled as implementation issue.

## Slide 5: Way forward on Test Model Definition
NB-IoT carriers shall be configured according to N-TM as defined in TS 36.141 subclauses 6.1.3, 6.1.4, 6.1.5 and 6.1.6.
NR carriers shall be configured according to NR-FR1-TM1.1 as defined in subclause 4.9.2 of TS 38.141-1, and data content of physical channels and signals as defined in subclause 4.9.2.3 of TS 38.141-1. One PRB is punctured to make room for NB-IoT PRB.
For TDD, use uplink/downlink configuration (with 15 kHz SCS) in Table 5.5.3-1 in TR 37.824 to derive the NR carriers to align with E-UTRA TDD uplink/downlink configuration #1 and special subframe #8.