## Slide 1: WF on side conditions of SSB based and CSI-RS based beam correspondence tests
Apple Inc.
3GPP TSG-RAN4 Meeting #93 R4-1916172 Reno, USA, 18-22 Nov, 2019

## Slide 2: Background
The following contributions on the topic of beam correspondence in Rel-16 were discussed:
ref | tdoc | source | title
[1] | R4-1913145 | Qualcomm Incorporated | FR2 Beam Correspondence using SSB only
[2] | R4-1913205 | Qualcomm Incorporated | Beam management CSI-RS design for BC requirement
[3] | R4-1913327 | Samsung | Discussion on Rel-16 Beam Correspondence Side Condition
[4] | R4-1913521 | Samsung | Discussion on more enhancement to beam correspondence in Rel-16
[5] | R4-1913537 | Apple Inc. | Views on beam correspondence enhancements
[6] | R4-1913901 | MediaTek Inc. | Beam correspondence for initial access
[7] | R4-1913948 | LG Electronics | Enhanced beam correspondence in rel-16 at FR2
[8] | R4-1914127 | NTT DOCOMO, INC. | Views on beam correspondence enhancement in Rel-16
[9] | R4-1914142 | Ericsson, Sony | Test configuration for beam correspondence during initital access
[10] | R4-1914275 | Nokia, Nokia Shanghai Bell | FR2 BC enhancements
[11] | R4-1915041 | Sony | Enhanced reporting for beam correspondence in poor SNR condition
[12] | R4-1915042 | Sony, Ericsson | Views on SSB only and CSI-RS only beam correspondence
[13] | R4-1915316 | Qualcomm Incorporated | On FR2 Initial access beam correspondence
[14] | R4-1915371 | Huawei, HiSilicon | On beam correspondence for Rel-16

## Slide 3: BC based on SSB
Strive to resolve the open issues associated with the side condition parameters by the next meeting
By RAN4 #94, RAN4 could specify BC based on SSB only unless RAN4 find critical technical problems, considering:
  Side condition feasibility
  Common understanding of UE behavior
  Performance difference with SSB + CSI-RS based BC
After stabilizing the configuration and requirement structure and confirming the feasibility, the optionality of this requirement can be discussed
Parameter | Value
SSB periodicity | 20 ms [1]
Use P1 CSI-RS configuration? | No
Use P3 CSI-RS configuration? | Alt. 1: Yes Alt. 2: No
Use tracking CSI-RS? | Yes
Tracking CSI-RS QCL info | qcl-TypeD=SSB
Tracking CSI-RS min SNR | TBD
PDCCH/PDSCH DM-RS QCL info | qcl-TypeD=TRS
SSB min SNR level | Alt. 1: 6 dB [1] [10] Alt. 2: 13 dB [14]
(note) | RAN4 didn’t assume more than [1] SSB indices should be transmitted SSB use configuration for Rel-15 which is specified in 38.508 per agreed in RAN4 #92bis meeting

## Slide 4: BC based on CSI-RS (configurations)
Parameter | Value
P1 CSI-RS periodicity | Alt.1: P1 CSI-RS is configured with [TBD] ms periodicity, the QCL (qcl-TypeD) relation is configured as ‘SSB’ Alt.2: P1 CSI-RS is not configured; instead aperiodic P2 CSI-RS can be considered if necessary. If P2 CSI-RS is supported, its qcl-TypeD is ‘SSB’ [2] Alt.3: P1 CSI-RS is configured with [TBD] ms periodicity, the QCL (qcl-TypeD) relation is configured as ‘none’
P3 CSI-RS repetitions per resource set | Alt. 1: maxNumberRxBeam in UE capability IE of MIMO-ParametersPerBand Alt. 2: 8
P3 CSI-RS configuration repetition | on
P3 CSI-RS trigger | Alt.1: once P1 CSI-RS is finished Alt.2: once every SSB cycle (20 ms) if P1 CSI-RS is not configured * The test time for Alt.1 is assumed less than or equal to Alt.2
Tracking CSI-RS periodicity | reuse Rel-15 60 kHz SCS: 40 slots for CSI-RS resources 1 and 2 120 kHz SCS: 80 slots for CSI-RS resources 1 and 2
P3 CSI-RS QCL info | Alt.1: Type D to P1 CSI-RS Alt.2: If P2 CSI-RS is transmitted; - Type A to TRS - Type D to P2 CSI-RS Otherwise; - Type C to SSB - Type D to SSB
P1 CSI-RS QCL info | Alt.1: P1 CSI-RS is transmitted and the QCL relation is configured as ‘SSB’ [14] Alt.2: P1 CSI-RS is not transmitted [2] Alt.3: P1 CSI-RS is transmitted and the QCL relation is configured as ‘none’

## Slide 5: BC based on CSI-RS (side conditions)
How to achieve “CSI-RS only” condition
  Method 1: DUT is configured with an active BWP containing no SSB
  Method-2: SSB in wide beam and CSI-RS in fine beam from TE
  Method-3: SSB and CSI-RS are present, but SSB’s PSD is back-off by XdB from CSI-RS
    X will be chosen during the RAN4#94 meeting
  A single method will be chosen during the RAN4 #94 meeting
CSI-RS min SNR level:
  Alt1: 6 dB
  Alt2: same as SNR chosen for SSB in SSB-only BC test
After stabilizing the configuration and requirement structure and confirming the feasibility, the optionality of this requirement can be discussed