## Slide 1: WF on FR2 test methodology enhancement
Apple Inc., CAICT, ...
3GPP TSG-RAN4 Meeting #92bis R4-1916177 Chongqing, China, 14-18 Oct, 2019

## Slide 2: References
ref | tdoc | source | title
[1] | R4-1913252 | Rohde & Schwarz | Views on test methods for high DL power and low UL power TCs
[2] | R4-1914608 | MVG Industries, SONY | View on NFTF and DNF test methods
[3] | R4-1915080 | Keysight Technologies | On White Box Testing
[4] | R4-1915081 | Keysight Technologies | On Relaxation of Low UL and High DL Test Cases
[5] | R4-1913147 | Qualcomm Incorporated | On FR2 OTA testability of UE Tx Modulation Quality requirements
[6] | R4-1913523 | Samsung | Discussion on polarization mismatch for UL TX test
[7] | R4-1913547 | Apple Inc. | FR2 test method enhancement informal email discussion on the polarization basis mismatch objective
[8] | R4-1913674 | MediaTek Inc. | FR2 SISO enhancement for polarization mismatch
[9] | R4-1913941 | LG Electronics | Discussion on EIS test methodology for polarization mismatch
[10] | R4-1913960 | LG Electronics Polska | EIRP test methodology for polarization mismatch
[11] | R4-1914795 | Rohde & Schwarz | Options to optimize the polarization mismatch
[12] | R4-1915061 | Anritsu Corporation | Views on polarization mismatch between DUT and TE
[13] | R4-1915082 | Keysight Technologies | On Minimizing Impact of Polarization Basis Mismatch
[14] | R4-1915390 | Huawei, HiSilicon | On EIS test metric
[15] | R4-1913148 | Qualcomm Incorporated | On enabling single AoA testing for FR2 inter-band DL CA
[16] | R4-1913253 | Rohde & Schwarz | Views on testability of inter-band CA in FR2
[17] | R4-1913548 | Apple Inc. | Views on test methodology for inter-band
[18] | R4-1913931 | Anritsu Corporation | Test system for inter-band DL CA in FR2

## Slide 3: Background
For Objective 1 a list of questions was developed to clarify the scope of potential enhancements targeting Track 2
An informal email discussion related to Objective 2 was held prior to the RAN4 #93 meeting with company views captured in [7] for information
Views were exchanged on the EIRP measurement, EVM measurement, and EIS metric aspects related to Objective 2

## Slide 4: Objective 1: questions to be resolved
Q1: Is the industry willing to accept specialized test systems with limited scope that only fulfill the needs for specific requirements?
Q2: Are enhanced testability methods required to perform beam peak search and spherical coverage tests?
Q3: Is the industry willing to consider declaration by the manufacturer as a technique to improve test accuracy (e.g. white box approach)?
Q4: If yes on Q2 & Q3, is the industry willing to consider declaration by the manufacturer which antenna panel is active in any UL/DL test direction and the detailed locations of the panels within the DUT?
Q5: If no on Q2 and yes on Q3, is the industry is willing to declare the location of the active panel for the beam peak or the beam peak direction?
Q6: How sensitive is the UE beam management to the amplitude and phase variation of the DL signal over a single array and over the whole device?
Q7: Shall DUT Antenna Configuration 3 (any phase coherent antenna panel of any size, e.g. sparse array) be excluded from the scope of test method enhancements?
Feedback from interested companies and, in particular, OEMs and chipset vendors to these questions is requested

## Slide 5: Objective 2: EIRP measurement
RAN4 assumes the UE architecture is capable of transmission in 2 polarizations
  Single pol. transmitters not precluded, if they meet core requirements
If RAN4 finds a difference conflict between the core requirement and EIRP measurement procedure, then this issue can be addressed with the enhancement
RAN4 assumes the UE architecture is capable of simultaneous 2 Tx
  A decision whether intermittent UE transmission in 1 polarization (e.g. polarization specific beam correspondence) can be assumed is needed
  If the above is confirmed, whether a UE declaration can be used to inform the test methodology is FFS
Test methodology techniques under consideration:
  Method 0: No change to the measurement procedures in TR38.810
  Method 1: “H&V simultaneous operation with 2-port CSI-RS beam management by TE” [8]
  Method 2: “Keep H&V non-simultaneous operation by TE, but change test procedure to Link_V → Link_H → UE_Beam_Lock → Measurement_V → Measurement_H” [8]
  Method 3: “H&V non-simultaneous operation by TE with additional 45 deg link” [8]
  Method 4: Different approach for calculating total EIRP [10]
  Method 5: Polarization sweep of the DL signal [R4-1911503]
  Method 6: The use of CP for the DL signal and UL signal measurement [R4-1911503]
  Method 7: Test mode for certification purpose to force the UE to transmit on both polarizations
  Method 8: The use of Elliptical Polarization for the DL [11]
  Other methods are not precluded
Analysis on the feasibility of each solution is requested to enable a down-selection of methods

## Slide 6: Objective 2: EVM measurement
Test methodology techniques under consideration:
  Method 0: No change to current test procedure and test mode in TS38.521-2 [12]
  Method 1: OTA receiver with coherent combining of Rx signals received by TE in two orthogonal polarizations [5]
  Method 2: TE search for optimal polarization angle to receive UL signal with a single polarization receiver [5]
  Method 4: The use of Elliptical Polarization for the UL [11]
Refinement of EVM measurement in case of single pol receiver
  Method 13: Weighted EVM [11]
Analysis on the feasibility of each solution is requested to enable a down-selection of methods

## Slide 7: Objective 2: EIS metric
RAN4 made an assumption on UE Rx architecture in Rel-15
  See [R4-1706067] at right ->
A decision is needed whether UE reception in 1 polarization (e.g. 1 Rx UE) can be assumed
Test methodology techniques under consideration:
  Method 1: TE to measure {EIS0, EIS30, EIS60, EIS90, EIS120, EIS150} and update EIS metric as described in [14]
    The sweep step could be further evaluated
  Other method is not precludedFFS

## Slide 8: Objective 3
Companies are encouraged to take the FR2 inter-band CA agreements [R4-1916024] from the FR2 RF enhancement work item into account when planning contributions for the next meeting
Study the achievable PSD difference for 28+39GHz CA under the assumption of 1AoA test setup with single feed antenna.
Study the side conditions of polarization relationship between 28GHz and 39GHz. (i.e. combination of polarization. 28G v-pol + 39 G v-pol, 28G h-pol + 39G v-pol, 28G v-pol+ 39G h-pol, 28G h-pol + 39G h-pol.)

## Slide 9: Next Steps
An email discussion period after RAN4 #93 is needed to capture written responses from interested companies to the questions related to Objective 1 as well as views on open issues related to Objective 2 and 3
An official offline conference call after RAN4 #93 is needed to collect companies’ input on the open issues identified in this way forward in order to more efficiently prepare for RAN4 #94
  Study Item Rapporteur to arrange the call and provide details via the RAN4 email reflector