## Slide 1: WF for spherical coverage enhancement for FR2
NTT DOCOMO, Verizon, KDDI, AT&T, SoftBank Corp., T-Mobile USA Inc., CHTTL, Vodafone, Nokia…
R4-1916184
3GPP TSG-RAN WG4 Meeting #93
Reno, NV, USA, 18-22 Nov 2019
Agenda: 9.14.10

## Slide 2: Background
PC 3 Spherical coverage enhancement is included in the scope of Rel-16 UE RF FR2 enhancement WI[1].
  This work item will also study if FR2 UE spherical coverage requirements for PC3 for >20%-tile can be defined.
There were several solutions are provided in the previous meetings
  Specify the EIRP spherical coverage value at 20%-tile[2]
  Signalling approach to enhance CDF %-tile for EIRP spherical coverage while peak EIRP is same as that of Rel-15[3][5]
  New power class to enhance both peak EIRP and EIRP spherical coverage[4]
  Removing multi-band relaxation[6]
However, there also concerns raised from some vendors about the feasibility of spherical coverage enhancement.

## Slide 3: WF
Companies are encouraged to provide their feasibility studies in RAN4#94 for handheld UE
  Possible enhancement 1: add a different %-tile for EIRP spherical coverage value, i.e., 11.5dBm for n257, n261, n258, and 8dBm for n260 or other lower EIRP spherical coverage value
  Possible enhancement 2: increase current 50%-tile EIRP spherical coverage value by Y dB
    Bands for feasible studies can be prioritized as n257, n261, n260, n258
  * If needed, provide parameters related to UE form factor assumption to achieve enhancement of spherical coverage requirement
RAN4#94 should decides to take the below options:
  Alt1: Enhance spherical coverage requirements
    Option1: Enhance %-tile for EIRP spherical coverage value[2][3][5]
    Option2: Enhance dBm value for 50%-tile of EIRP spherical coverage value[6]
  Alt2: Introduce the new power class for handheld UE[4]
  Other options are not precluded
Evaluation of feasible studies will be captured in TR 38.831 in RAN4#94.

## Slide 4: References
[1]: RP-192227 Revised WID on NR RF Requirement Enhancements for FR2, Nokia, Nokia Shanghai Bell, RAN#85
[2]: R4-1909884 Enhanced spherical coverage requirement for FR2 PC3 UE, Nokia, Nokia Shanghai Bell, RAN4#92
[3]: R4-1909981 FR2 power class enhancement, NTT DOCOMO, INC., RAN4#92
[4]: R4-1911594 Enhanced spherical coverage requirement for FR2 PC3 UE, Nokia, Nokia Shanghai Bell, RAN4#92bis
[5]: R4-1911715 Power class frame work in FR2 , NTT DOCOMO, INC., RAN4#92bis
[6]: R4-1913146 On Improvement of Spherical Coverage for PC3, Qualcomm Incorporated, RAN4#93