## Slide 1: WF on IAB TS spec structure and terminology
Qualcomm
R4-2002123
3GPP TSG-RAN WG4 Meeting #94
E-meeting, 24 Feb. – 6 Mar., 2020
Agenda item: 8.5.1

## Slide 2: Background
During the last meeting, an email discussion with Tdoc #R4-191600 was initiated after the meeting.
Companies reached consensus regarding slide 3-5 of this deck and the updated IAB TS spec during the email discussion.
We are now formally submitting the outcome of the email discussion, i.e., the WF and the updated TS spec, to RAN4 94.

## Slide 3: Background
During the last meeting, RAN4 RF session discussed IAB spec structure and terminology.
Companies discussed whether IAB TS spec will be written in a completely self-contained manner or whether individual sections of IAB TS spec should refer to NR BS and UE specs as much as possible.
Writing IAB spec in a completely self-contain manner means that
  IAB TS 38.174 needs to be evaluated as impacted one of the impacted specs:es for future new feature/correction
    separate CRs will may be needed whenever one makes a minor change in BS or UE spec.
One can avoid this duplication effort by referring to NR BS and UE specs as much as possible
Separate CRs will may be needed whenever one makes a minor change in BS or UE spec.

## Slide 4: Background
Referencing implications:
  as referencing means strong connection to the spec that is referenced to. There is a need to clarify the rules and implications before setting such high level principle.
IAB DU: referencing is ”Strong” term, it means ”interchangable” with source spec, req change at one spec change will change the same req at another spec
  Rule:“ IAB DU reusing the BS spec”,
  Scope relation: BS spec contain IAB DU spec, not the other way around
  Implication:
    here “reusing” requirement means with correct terminology change and/or apply to correct paragraph and table, Additional text to describe how this reference would apply is needed, either generically or down to separate section/req level. The “delta” info need to be added.
    Also future BS spec updates for correction/new feature will not change this rule, meaning there is no need to examine the IAB TS spec. However, it is questionable weather “delta” info need to be re-visited. If it did, IAB TS spec need to be evaluated as one of impacted spec anyway.
    if there were IAB specific feature which impact IAB DU, BS spec (source spec) need to be updated
IAB MT: referenceing is ”weak” term, there is no OTA FR1 UE spec, so OTA IAB FR1 spec referencing to any of requirement to FR1 UE spec will be confusing
  Rule: Selectively, some UE spec requirement text can be referenced if IAB MT req is the same with UE at the time of the spec written.
  Scope relation: UE spec and IAB MT spec maybe overlap in some of requirement, one spec cannot contain the other
  Implications:
    There are requirments cannot be referenced and so deviation to the UE spec (source spec) is expected.
    Future UE spec updates for correction/new feature need to examine the IAB MT Spec anyway, the ”rule” may not hold, i.e reference could be changed to new text if it reasonable to do so.
      IAB TS 38.174 need to be evaluated as impacted one of Spec:es for future new feature/correction
    here “reusing” requirement means with correct terminology change and apply to correct paragraph and table, Additional text to describe how this reference would apply is needed, either generically or down to separate section/req level.

## Slide 5: Proposal
Option 1: Referencing
  If the requirements of an IAB-DU or an IAB-MT are same as those of a gNB or a UE, 38.174 will may refer to the corresponding sections of gNB and UE specs. Additional text will only be added to highlight the differences from the source specs. The condition is that future IAB specific feature need update the source BS spec which maybe need some IAB specific wording. Or update the “delta” info in IAB TS spec.
  If the requirements text of an IAB-DU or an IAB-MT are same as those of a gNB or a UE, 38.174 will may refer to the corresponding sections of gNB and UE specs. Additional text will only be added to highlight the differences from the source specs. How to resolve the issue when feature/correction applied to source spec would not apply to IAB MT need to be discussed, one solution maybe additional IAB specific wording will be needed in source spec to clarify this. Another solution is to scope out the new changes/modification in IAB spec, “delta” info text update is needed.
Option 2: Self contained
  Good readability without thinking hard how to write good “delta” info text.
Proposal: Keep the two options above at this stage and evaluate them at during the meeting and cross check to each other.
  Note: It may be good to see how easy/difficult of each option is in the end and decide later.
Note:
The key question is that if there is a need to evaluate the IAB TS when either BS spec or UE spec change due to future BS correction/new feature and UE correction/future feature. It seems such evaluation cannot be avoided, then referencing can only save effort on the editing of TS spec, and drawback is that readability is not good.
Same text should be used in all sections with these references to clarify that requirements apply to IAB-DU or IAB-MT
  E.g. Same requirements applicable in section X.X of 38.104 apply to IAB-DU.
  Note: Above will reduce duplication efforts and ensure that any change in original spec will be automatically replicated in 38.174.