## Slide 1: WF on NR Mobility Enhancements RRM requirements
Intel Corporation
3GPP TSG-RAN WG4 Meeting #94-e R4-2002224
Electronic Meeting, 24 Feb. – 6 Mar., 2020

## Slide 2: Background
Agreements in this way forward are based on email discussion in R4-2002173 Email discussion summary for RAN4#94e_#50_NR_Mob_enh_RRM

## Slide 3: Agreements for DAPS handover
Issue 1-1: Interruption in intra-frequency DAPS HO D1
Agreement:
X value:
Option 1: 3 (slots)
Option 2: 4 (slots)
Issue 1-2: power imbalance
Agreement: Companies are encouraged to provide further analysis on side condition of power imbalance for intra-frequency DAPS HO.
 | NR Slot length (ms) | Interruption length X (slotsnote 1)
0 | 1 | [1]
1 | 0.5 | [2]
2 | 0.25 Note 2 | [X]
Note 1: The same SCS of source cell and target cell is assumed. Note 2: Both source cell and target cell is on FR1. |  | 

## Slide 4: Agreements for DAPS handover (cont.)
Issue 1-3: When CBW relationship is different from that of BWP
Agreement: no requirements for CBW relationship is different from that of BWP
Issue 1-4: Restriction on BWP for inter-frequency DAPS HO:
Agreement: RAN4 will not define requirement for the case where the BWP of target cell is partial overlapped with the BWP of source cell in frequency domain.
Issue 1-5: Requirement for inter-FR DAPS HO:
Agreement: Both FR1-FR2 and FR2-FR1 DAPS handover requirements need to be standardized.
Other issue: Synchronization assumption
Agreement: Companies are encouraged to provide analysis on if requirement for intra-frequency DAPS handover are only applied for synchronous case

## Slide 5: Agreements for CHO
Issue 2-1: UE preparation time
Agreement: TRRC_2/TCHO_execution = 10ms
Issue 2-2: Reformulate Tmeasure:
Agreement: Tmeasure is updated to cover the following two parts:
Delay uncertainty which is the time from when the UE successfully decodes a CHO command until a condition exists at the measurement reference point which will trigger the CHO.
Measurement event evaluation delay which begins once the delay uncertainty ends, and ends when the UE starts to execute CHO

## Slide 6: Agreement for Conditional PSCell change
Issue 3-1: Conditional PSCell addition/release
Agreement: Requirements for conditional PSCell addition/release are not needed in this work item.
Issue 3-2: Where to capture conditional PSCell change
Agreement: conditional NR PSCell change requirement will only be introduced in TS38.133
Issue 3-3: Conditional PSCell change delay:
Agreement: Tconfig_PSCell_Conditional = TRRC_processing + Tmeasure + TUE_preparation + Tprocessing + T∆ + TPSCell_ DU + 2 ms
Note: Agreement of Tmeasure can be found in the next page. Definitions of rest term can be found in R4-2002224

## Slide 7: Agreement for Conditional PSCell change (cont.)
Issue 3-3: Tmeasure in conditional PSCell change delay:
Tmeasure includes the following two parts:
Delay uncertainty which is the time from when the UE successfully decodes a CPC command until a condition exists at the measurement reference point which will trigger the CPC .
Measurement event evaluation delay which begins once the delay uncertainty ends, and ends when the UE starts to execute CPC
Issue 3-4: Interruption during conditional PSCell change:
The interruption at conditional PSCell change shall be allowed only after the measurement evaluation delay.