## Slide 1: Way Forward on parameters and test methodology for URLLC ultra-low BLER test
R4-2002422
Moderator (Ericsson)

## Slide 2: Topic #1: Key parameters for ultra-low BLER test time estimation

## Slide 3: Agreements from first round
Decision frequency (N) is 1 (i.e. early pass/fail evaluation on every detected block error)
SCS for UE: 15kHz for FDD, 30kHz for TDD
SCS for BS: 15kHz and 30kHz
TDD pattern: 7D1S2U (S=6:4:4) for UE

## Slide 4: Agreements from second round
Slot aggregation factor:
  Slot aggregation factor is 1 if X (see slide 12) is <3dB
  Slot aggregation factor is [1, 2] if X>=3dB

## Slide 5: Items needing further discussion next meeting
Requirements and tests for FR2:
  Option 1: Create requirements for FR2. No explicit applicability rule needed. Option 2: Create requirements for FR2 with applicability rule Proponents of option 2 please clarify what applicability rule you propose
  Option 3: Do not create requirements for FR2
TDD patterns for BS
  Proposals FR1
    Option 1: 3D1S1U (S=10:2:2) for 15kHz, 7D1S2U (S=6:4:4) for 30kHz
    Option 2: SU or DSUU

## Slide 6: Topic #2: Other parameters for ultra-low BLER test

## Slide 7: Agreements from first round
CP-OFDM
  DFT-S-OFDM is FFS
Antenna configuration for BS: 1x2
Antenna configuration for UE: 2x2 + 2x4 (2x4 agreed in 2nd round) ULA low with applicability rule
No PT-RS for FR1
PUSCH configuration: Start symbol 0, length 14 symbols
PDSCH configuration: Mapping type A, start symbol 2, length 12 symbols
MCS table: Use low spectrum efficiency MCS

## Slide 8: Agreements from second round
Number of RB and bandwidth for PDSCH
  Full bandwidth for 10MHz/15k SCS and 40MHz/30Kscs
PUSCH mapping type
  Type A and type B with applicability rule

## Slide 9: Items needing further discussion next meeting
PT-RS and DM-RS configuration for PUSCH
  Option 1: 1+0
  Option 2: 1+1
  Option 3: 1+0 and 1+1 with applicability rule
DM-RS configuration for PDSCH
  Option 1: Zero additional DM-RS
  Option 2: One additional DM-RS
Number of RB for PUSCH
  Option 1: 25 RB
  Option 2: 65 RB
  Option 3: Full bandwidth for 5MHz/15k SCS and 10MHz/30Kscs
  Option 4: Full bandwidth with 10MHz/15k SCS and 40MHz/30k SCS
  Option 5: Full bandwidth
  Other options not precluded

## Slide 10: Items needing further discussion next meeting
Bandwidth for PUSCH
  Option 1: 5MHz for 15k SCS, 10MHz for 30k SCS
  Option 2: 10MHz for 15k SCS, 40MHz for 30k SCS
  Option 3: 5/10/20MHz for 15k SCS, 10/20/40/100MHz for 30k SCS, applicability rule to ensure just one test
  Option 4: Option 1+option 2
  Other options not precluded

## Slide 11: Topic #3: Test method

## Slide 12: Agreements from first round
  Reformulate the discussion as follows:
    Test requirement = SNR for 10^-5 + IM + [X]
    X is FFS and could be zero
    FFS whether X appears in the core spec or test spec, or is just considered part of IM

## Slide 13: Items needing further discussion next meeting
Issue 3.5.1: Value for X
  Option 1: X is zero
  Option 2: Not higher than ~0.5 dB
  Option 3: More than 1dB, prefer 3dB
  Other options not precluded
Issue 3.5.2: Whether X is specified in the core spec and if so whether it is explicit or part of the IM
  Option 1: Core spec and explicit
  Option 2: Core spec and implicit (in IM)
  Option 3: Not in core spec
  Note: Issue is only applicable if X is non-zero
Issue 3.5.3: Whether X is specified in the conformance spec, and if so whether it is explicit or part of the TT
  Option 1: Conformance spec and explicit
  Option 2: Conformance spec and implicit (in TT)
  Option 3: Not in Conformance spec
  Note: Issue is only applicable if X is non-zero

## Slide 14: Topic #4: Number of tests to define

## Slide 15: Items needing further discussion next meeting
Number of requirements
  Option 1: zero requirements/tests
  Option 2: One requirement/test
  Option 3: >1 requirements, but only one test (using applicability rule)
  Option 4: more than one requirement and more than one test
  Other options not precluded
CQI testing at ultra-low BLER
  Option 1: Define CQI testing with ultra-low BLER
  Option 2: Do not define CQI testing with ultra-low BLER