## Slide 1: WF on IAB-MT ACS,IBB and ACLR in FR1
ZTE
R4-2002490
3GPP TSG-RAN WG4 #94e
24th Feb.2020 – 6th Mar. 2020

## Slide 2: Background
Tentative agreement in discussion #82 of RAN4#94-e to define two classes for IAB-MT, out of which at least one is for macro/planned/high power deployments
Coexistence simulation results have been performed for layout 1 and layout 2 addressing HetNet deployment and homogenous deployment micro/planned
Coexistence results among companies differ between the layouts and there are two options proposed among companies, either to reuse FR1 UE ACLR requirement with lower minimum output power or reuse FR1 BS ACLR requirement with higher minimum output power.

## Slide 3: WF
    For IAB MT ACS requirement:
    Option 1: reuse the BS requirement as 46dB ACS
    Option 2: reuse the UE requirement as 33dB ACS
    For IAB MT IBB requirment
    reuse the BS requirement if 46dB ACS applied for IAB-MT
    Option 2: FFS if 33dB ACS applied for IAB MT
    For IAB-MT ACLR and minimum output power
    Option 1: 30dBc with minimum output power=10dBm
    Option 2: 45dBc with higher minimum output power =FFS
    IAB-MT minimum output power should derive from minimum distance between IAB-DU and IAB-MT associated with IAB-MT class and Tx dynamic range could cover that.

## Slide 4: References:
  R4-2001873 in-band blocking and ACS of IAB MT, Ericsson
  R4-2000972 simulation results for FR1 IAB coexistence study, ZTE
  R4-2001865 IAB-MT ACLR , Ericsson
  R4-2000977 In-band blocking for FR1 IAB MT, ZTE
  R4-1910838 FR1 IAB co-existence study,CMCC
  R4-1911735 simulation results for FR1 IAB coexistence study,ZTE
  R4-1912009 Coexistence simulation results for FR1 - layout 1,Ericsson
  R4-1912011 Coexistence simulation results for FR1 - layout 2,Ericsson
  R4-1914163 Simulation results for IAB in FR1,Huawei
  R4-1911394 Updated simulation result for layout 1, Samsung