## Slide 1: WF on testability of transient period capability
Huawei, HiSilicon, Starpoint, OPPO, China Unicom, LGE, [Vivo], [Unisoc]
R4-2002813
3GPP TSG-RAN WG4 #94e
Feb 24th – Mar 06th, 2020
Electric meeting

## Slide 2: Background: Summary of 1st round discussion
 | Comments |  | Comments
1 | whether RMS EVM over 1 slot can represent the transient period capability View 1: no relation with testability View 2: relates whether TE can capture the accurate transient period | 7 | whether RMS EVM with DFT-OFDM measurement similar with LTE can be tested for transient period View 1: can use current LTE procedure View 2: can sue the current LTE procedure with exclusion period matched. View 3: can not take the procedure defined for LTE
2 | For RMS EVM over 1 slot, whether EVM measurement procedure on equalizing is clear for UE View 1: existing procedure for equalization does not need any modification. View 2: out of scope to compare equalization procedure for BS and UE View 3: different equalization procedure will lead to different EVM measurement result | 8 | UL DL configuration: View 1: no relation with testability View 2: TDD pattern Figure 2.3-2 from R4-2000442 View 3: further discuss after testability is solved
3 | For RMS EVM over 1 symbol, how to define EVM measurement procedure in the spec View 1: object to the discussion in RAN4 that have new WI study on RMS EVM over 1 symbol View 2: Create new section in Annex clarifying assumptions View 3: RAN4 need further study on the test procedure for 1symbol case, new WI/SI would be an option. | 9 | how to calculate EVM for symbols in which the transient occurs View 1: no relation with testability View 2: calculated for the two symbols impacted by the transient
4 | whether 20dB power change can represent the maximum power change in the network, if not, whether TE can provide the test condition for the maximum power change View 1: no relation with testability View 2: it has not been proposed or discussed in any paper View 3: TE can only provide about 20dB dynamic range for EVM test View 4: Provide analysis in R4-1915367 that the maximum range can be up to 55dB | 10 | EVM budget for symbol where the transient occurs View 1: no relation with testability View 2: evaluate further or use the current value in [2] View 3: relaxation on EVM may have impact on high order modulation
5 | How to ensure the transient period is symmetrically positioned? View 1: not related to testability View 2: only exclusion period is symmetrically placed View 3: UE always reports worst case situation that could be tested View 4: no mechanism to guarantee the transient period is symmetrically placed and TE may not capture any transient occurs on the after symbol. | 11 | Issue 4-4: LS to RAN View 1: send LS to RAN plenary to inform that RAN4 has agreed that testability of the new feature on transient capability View 2: no reason to send LS View 3: Send LS to RAN plenary to inform that RAN4 cannot make consensus on testability
6 | whether EVM=min(EVML, EVMH) can differentiate UE with different transient period ability View 1: finer resolution may need to use a higher SCS View 2: with the rounding to the upper 1us the test is valid View 3: it is highly depends on the SCS UE can support, UE is not mandatory to support every SCS. |  | 

## Slide 3: WF1: largest power change range between 2 UL transmissions
Power control equation from TS 38.213:
Where P0_PUSCH and P0_PUCCH are configured separately under one serving cell, in which:
P0_PUSCH= P0_NOMINAL_PUSCH + P0_UE_PUSCH, P0_NOMINAL_PUSCH is specified with range {-202,24} dBm in TS 38.331
P0_PUCCH= P0_NOMINAL_PUCCH + P0_UE_PUCCH, P0_NOMINAL_PUCCH is specified with range {-202,24} dBm in TS 38.331
NR configuration parameters in a real network from different gNB vendors are provided as below:
gNB Vendors No. | P0_PUSCH | P0_PUCCH | RB change 1RB->273RB | Largest power change between 2 UL transmissions
1 | -86 | -104 | 24dB | 42dB
2 | -70 | -104 | 24dB | 58dB
3 | -73 | -100 | 24dB | 51dB
The largest difference in real network between 2 consecutive physical channel UL transmissions could be up to 58dB.
In the 1st round discussion, TE vendor provides the comments:
The largest power change dynamic range TE can provides for EVM measurement is 20dB
Conclusion: the largest power change dynamic range TE can provides can not match the power change range under real networks

## Slide 4: WF2: testability for CP-OFDM waveform
Initial consensus in RAN4 for CP-OFDM:
It is not possible to exclude transient period from the EVM FFT samples for CP-OFDM [3], since it is directly mapped to subcarrier in frequency domain, removing any exclusion window in time domain will destroy the data on each RE.
Exclusion window can not be different with EVM window length defined in TS 38.101-1 Annex [3].
Analysis assumption: Transient period is symmetrically positioned across the boundary [3]
The current EVML window and EVMH window specified in TS 38.101-1: it shows EVMH window is almost identical with 75% CP-length
SCS | EVML window | EVMH window
15kHz | 1.175 | 3.525
30kHz | 0.5875 | 1.7625
60kHz | 0.2937 | 0.8812
Consensus in RAN4 #94e meeting:
For CP-OFDM, it is not possible to verify the exact UE transient period duration when transient timing advance is set constant and equal to -75%CP length using only EVM=min(EVML,EVMH) as a metric.[2]
Currently there is no guaranteed method that the transient period is symmetrically positioned.[1]

## Slide 5
WF3: testability for DFT-s-OFDM waveform
For DFT-s-OFDM, the assumption is: transient period is symmetrically shared on the boundary
For both before and after symbols/slots across the transient periods, the RMS EVM testability need to be considered
For the before symbol/sot, if RAN4 takes LTE procedure for NR, the test metric is EVM=max(EVML, EVMH)
For UE only support 15kHz, TE takes EVML as the EVM result means the lagging exclusion already excludes 3.525us data samples. The UE capability which is lower than 3.525us can not be tested.
For UE only support 15kHz and 30kHz, TE takes EVML as the EVM result means the lagging exclusion already excludes 1.7625us date samples. The UE capability which is lower than 1.7625 can not be tested.
The problems for after symbol/slot mentioned in CP-OFDM also exists for DFT-s-OFDM.
Conclusion: for DFT-s-OFDM, NR can not use the similar procedure defined for RMS EVM with power change in LTE
Before
symbol/slot
After
symbol/slot

## Slide 6
WF4: equalizing process for RMS EVM over 14 symbols is not specified clearly for UE
Equalizing process for UE specified in TS 38.521
Equalizing process for gNB specified in TS 38.104
Conclusion: equalizing process for RMS EMS over 14 symbols is not clearly defined for UE compared with the process for gNB.

## Slide 7
WF5: 1st symbol RMS EVM which transient period occurs
Some corresponding consensus in RAN4:
If pass/fail only relies on rms EVM/14OS, a UE could pass the test while not meeting its declared transient period. [3]
If 1st symbol RMS EVM for symbol where transient occurs is considered to verify transient period capability:
  Currently no specification on the test condition, assumption and processing procedure for RMS EVM/1OS [1] [4]
  Target EVM for 1st symbol with transient need to be relaxed [2][3]
Conclusion: comprehensive research and discussion are needed for 1st symbol RMS EVM on evaluating transient period in RAN4

## Slide 8
WF6: How to differentiate capabilities UE indicates
UE capability specified in TS 38.331 and TS 38.306 on numerology:
  SCS is optional supported for band combination
  For single carrier in FR1, 15kHz and 30kHz is mandatory, 60kHz is optional
testability assumption on transient period=150% CP using metric EVM=min(EVML,EVMH) in RAN4:
SCS [kHz] | 150 % CP length [s]
15 | 7.03
30 | 3.51
60 | 1.75
120 | 0.87
For UE do not support 60kHz, 2us transient period can not be tested
For UE do not support 30kHz and 60kHz, 4us transient period can not be tested
Since no 120kHz SCS is used in FR1, 1us transient period can not be tested
Conclusion: even all issues in WF1-WF5 are solved, transient period testability is highly dependent on the subcarrierspacing UE can support.

## Slide 9
WF7: How to handle with transient period capability in Rel-16
Testability for transient period capability shall be further studied in RAN4 which ensures UE capabilities indicated is captured accurately and the gNB gets the expected performance gain.
RF requirement on transient period capability(section 6.3.3 for on-on time mask) can be introduced in TS 38.101-1 in Rel-16 with no Rel-independent manner before all testability issues are addressed.
Test case for transient period capability is introduced in Rel-17 after the testability issues are solved.
Send LS to RAN and RAN5 to inform the above agreements.
The CR submitted in RP-192948 will be provided in RAN#87 meeting and should be further checked discussed in next RAN4 RAN#87 meeting based on the above agreements. It is encouraged interested companies provide more technical views on this CR for this introduction of this RAN4 RF new feature.

## Slide 10
Reference
[1] R4-2001757, “on transient period capability”, Huawei, HiSilicon, RAN4 #94e
[2] R4-2002143 ” EVM Measurements for FR1 Transient Period Capability Testability”, Skyworks, RAN4 #94e
[3] R4-1916016 “WF on transient period capability”. Qualcomm, Skyworks. RAN4 #93 meeting
[4] R4- 2000442 “Feasibility of on-to-on transient period measurement in FR1” Anritsu, RAN4 #94e
[5] R4-2002691 “email discussion summary on NR FR1 part 1_#18”, Huawei, HiSilicon