## Slide 1: WF on RRM measurement relaxation for Power Saving
CATT, Ericsson
3GPP TSG-RAN WG4 Meeting #94e R4-2002239
Electronic Meeting, Feb.24th – Mar.6th 2020

## Slide 2: Background
For information: Scenarios
  #1: Low mobility scenario
  #2: Not in cell-edge scenario
  #3: Low-mobility + Not in cell-edge scenario
RRM measurement relaxation methods for UE power saving in RRC_idle/inactive state
  Option 1: Allow RRM measurements with longer intervals
  Option 2: UE is not required to meet the intra-frequency and inter-frequency neighbor cell measurement requirements
Applicability of RRM relaxation methods when the relaxation criteria are fulfilled
 | Applicable RRM relaxation methods
Scenarios #1 | FFS: Option 1 and/or 2
Scenarios #2 | FFS: Option 1 and/or 2
Scenarios #3 | Option 2

## Slide 3: WF on RRM measurement relaxation
Applicability of RRM relaxation methods for scenario#1 and scenario#2:
  Scenario #1:
    Agreement - RRM measurement relaxation with longer intervals
  Scenario #2:
    Agreement - RRM measurement relaxation with longer intervals
FFS on the scaling factor of measurement interval
  Option 1: Fixed value
    FFS on one fixed value for both scenario#1 and scenario #2
    FFS on separate values for scenario#1 and scenario #2
  Option 2: Network configurable value
  FFS on the transition period between scenario#1 or scenario#2 and scenario#3
    Option1:
      When switching from scenario#2 to scenario#3, UE shall fulfill the requirements corresponding to scenario#2 for N DRX cycles and thereafter switch to requirements corresponding to scenario#3
      When switching from scenario#3 to scenario#2, UE shall fulfill the requirements corresponding to scenario #2 immediately.
    Other option is not precluded.

## Slide 4: WF on RRM measurement relaxation
RRM measurement relaxation for inter-frequency layer with higher priority
  Option 1: (CATT, Vivo, CMCC, Huawei, LGE, OPPO, Apple, MediaTek)
    When Srxlev > SnonIntraSearchP and Squal > SnonIntraSearchQ, no relaxation of the current measurement delay requirement is expected for inter-frequency measurement with higher priority.
    When Srxlev ≤ SnonIntraSearchP or Squal ≤ SnonIntraSearchQ, the relaxed requirement for the frequency layer of higher priority shall use the same relaxed measurement requirement as those for the frequency layer of equal/lower priority.
  Option 2: (Ericsson)
    Measurements of higher priority carriers shall not be relaxed in high mobility scenarios (scenario #2)
  Option 3: (Nokia)
    Measurements of higher priority carriers shall not be relaxed

## Slide 5: WF on RRM measurement relaxation
RRM measurement relaxation by reducing the number of frequency layer to be measured
  No consensus to introduce the RRM measurement relaxation by reducing the number of frequency layer in RAN4 94e.
  Interested companies are encouraged to provide analysis on achievable power saving from reducing number of frequency layers for intra/inter-frequency measurements in RAN4 94bis
EMR impact in power saving mode
  Option 1: Up to UE’s implementation(CATT, Vivo)
  Option 2: EMR frequency layer shall not be relaxed if T331 is running (LGE, Nokia, Qualcomm, CATT, OPPO, CMCC, Apple, Ericsson, ZTE, Intel)
  Option 3: EMR frequency layer shall be relaxed (Huawei, MediaTek)

## Slide 6: WF on RRM measurement relaxation
  RRM measurement relaxation threshold for inter-frequency measurement
  Option 1: Introduce carrier specific search thresholds for measurement relaxation(Vivo, Nokia, LGE)
  Option 2: Up to RAN2’s decision(CATT, Huawei, OPPO,CMCC, Apple, Ericsson, ZTE, MediaTek, Qualcomm)
  RRM impact due to cross-slot scheduling power saving technique
  Option 1: have RRM impact on DCI based delay requirement (CATT, Huawei)
  Option 2: no RRM impact (Ericsson, Nokia)
  Option 3: wait for RAN1 conclusion (Vivo, ZTE, Huawei)

## Slide 7: WF on 4Rx demod requirement impact due to MIMO layer adaption feature
Conclusion: Postpone discussion on Demod requirement impacts due to MIMO layer adaption to the WI performance part