## Slide 1: Way forward on demodulation and CSI requirement for NR eMIMO
Samsung
3GPP TSG-RAN4 Meeting #94-e
Electronic Meeting, Feb.24th - Mar.6th 2020
Agenda item: 8.11.3
R4-2002419
Document for: Approval

## Slide 2: Test Scope of Enhancement on Multi-TRP/Panel transmission
Define PDSCH requirement scheduled by multi-DCI based multi-TRP/Panel transmission
No PUCCH requirement for multi-PDSCH feedback
No multi-PDCCH requirement for multi-TRP/Panel transmission
No single-PDCCH requirement for multi-TRP/Panel transmission

## Slide 3: Test Scope of Enhancement on Multi-TRP/Panel transmission
Whether to define PDSCH requirement scheduled by single-DCI based multi-TRP/Panel transmission
  Option 1: Yes
  Option 2: No

## Slide 4: Test Scope of Enhancement on Multi-TRP/Panel transmission
No PDSCH requirements for URLLC multi-TRP transmission schemes with reliability transmission with lower BLER test metric (e.g., lower than 1% BLER) in Rel-16 NR eMIMO WI
Whether to define PDSCH requirements for URLLC multi-TRP transmission schemes with test metric @70% maximum TP
  Option 1: Yes
  Option 2: Deprioritize
  Option 3: No

## Slide 5: Test Scope of Enhancement on Multi beam operation
No performance requirement including demodulation and CSI reporting for L1-SINR measurement
No performance requirement including demodulation and CSI reporting for BFR for Scell
No performance requirement including demodulation and CSI reporting for DL/UL beam indication with reduced latency and overhead

## Slide 6: Test Scope of Enhancement on low PAPR RS
Whether to define PDSCH requirement based on Rel-16 DMRS enhancement
  Option 1: Define one DL test to verify receiver processing of Rel-16 DMRS enhancement
    Option 1a: if defined, existing UE performance test cases can be reused or replaced with Rel-16 DMRS configuration without requirements and other test parameters modification
    Option 1b: One new test case with test parameters modification
  Option 2: Not to define any new PDSCH performance requirement of Rel-16 DMRS enhancement

## Slide 7: Test Scope of Enhancement on low PAPR RS
No new PUSCH requirement based on Rel-16 DMRS enhancement for CP-OFDM
No new PUSCH requirement based on Rel-16 DMRS enhancement for DFT-s-OFDM
No new PUCCH requirement based on Rel-16 DMRS enhancement for DFT-s-OFDM

## Slide 8: Test Scope of Enhancement on full Tx power uplink transmission
No performance requirement including demodulation and CSI reporting for full Tx power uplink transmission

## Slide 9: Test Scope of Enhancement on MU-MIMO support
Define the PMI reporting requirement for Enhanced of Type II Codebook
No requirement for enhanced Rel-15 Type II codebook with Rank3/4
No requirement for UCI omission in CSI enhancement