## Slide 1: Way forward for NR UE URLLC performance requirements
Intel Corporation
3GPP TSG-RAN WG4 Meeting #94-e R4-2002428
Electronic Meeting, 24 Feb. – 6 Mar., 2020

## Slide 2: UE Performance requirements for high reliability (1)
Test parameters for UE FR1 URLLC demodulation requirement with high BLER
Agreements:
  TDD pattern: 7D1S2U, S=6D: 4G: 4U for 30 kHz SCS.
  MCS: MCS 5 in table 3.
  Propagation condition: TDLA30-10
  SCS & CBW:
    FDD: 15 kHz & 10 MHz
    TDD: 30 kHz & 40 MHz
  PDSCH configuration: Mapping type A, symbol length 12, starting symbol 2.
  Antenna configuration: 2x2 and 2x4, ULA low
  Target BLER: 1%
  Target Confidence level: 99%
  BLER is calculated after all transmission
  Max number of HARQ transmissions: 4

## Slide 3: UE Performance requirements for high reliability (2)
Open Issues
Whether to define UE FR2 URLLC requirements for high reliability
PDSCH aggregation level
  FDD
    Option 1: 4
    Option 2: 8
    Option 3: 2
  TDD
    Option 1: 4
    Option 2: 2

## Slide 4: UE Performance requirements for low latency (1)
PDSCH mapping Type B and PDSCH processing capability 2
Agreements for FR1:
Slots to be scheduled:
  FDD: All DL slots
  TDD: S slots with K1=0
Starting symbol: 2
Symbol length: 2
Slot aggregation level: 1
Max number of HARQ transmissions: 1
Verify PDSCH processing capability 2 and type B mapping together

## Slide 5: UE Performance requirements for low latency (2)
PDSCH mapping Type B and PDSCH processing capability 2
Open Issues
Whether to introduce UE performance requirements in FR2 for URLLC for low latency
For test parameters for FR1:
TDD Pattern (30KHz SCS)
  Option 1: 7D1S2U, S=6D:4G:4U
  Option 2: DDDSUUDDDD, S=6D:4G:4U
  Option 3: DSUU, S=12D:2G
  Option 4: DDDSU, S=10D+2G+2U
Number of HARQ Processes
  Option 1: 2
  Option 2: 4 or 8
Symbol length (L)
  Option 1: Also include 4os
  Option 2: Also include 7os with K1 = 1
  Option 3: Only 2os
Other test parameters
  Channel Model
  FRC
  Antenna configuration
  SCS/BW, Allocation

## Slide 6: UE Performance requirements for low latency (3)
Preemption indication for eMBB UE
Agreements:
No URLLC PI performance requirements
Time frequency set: 14x1
Number of symbols to be pre-empted: 2
Starting symbol to be pre-empted: 3
Test applicability for eMBB UE PI requirements: optional with UE capability signalling
Antenna Configuration: 2x2 and 2x4, ULA low

## Slide 7: UE Performance requirements for low latency (4)
Preemption indication for eMBB UE
Open Issues
Pre-emption periodicity
  Option 1: 10% probability with non-fixed scheduling in RAN4 spec (similar to CSI-RS trigger for PMI testing, also 10% probability with fixed scheduling in RAN5 spec) within 1 radio frame
  Option 2: 1 slot
  Option 3: 10% probability with fixed scheduling within 1 radio frame
Channel Model
  Option 1: TDLC300-100
  Option 2: TDLA30-10
FRC
  Option 1: 16QAM with modified FRC
  Option 2: QPSK
  Option 3: New FRC with 64QAM

## Slide 8: CQI reporting requirements for support of CQI table 3
Open Issues
Propagation channel for CQI reporting
  Option 1: AWGN
  Option 2: Fading channel
Target BLER
  Option 1: 10^-3
  Option 2: 10^-2
  Option 3: 10^-5
  Option 4: No BLER metric in fading channel
Test metric
  Option 1: Reuse existing BLER criteria test metrics
  Option 2: Percentage based of the maximum theoretical throughput
  Option 3: Reuse existing BLER criteria test metrics with a minimum median CQI
  Option 4: TP ratio with follow CQI vs median CQI and CQI not in set metric
Feasibility to define CQI reporting test case and FMCS case at the same SNR
  Option 1: Consider defining FMCS test and CQI reporting test under AWGN with the same SNR and define an applicability rule between CQI reporting test and FMCS test under AWGN to reduce the number of long tests