## Slide 1: WF on IAB definitions
Ericsson
3GPP TSG-RAN WG4 Meeting #94-e
Electronic Meeting, Feb.24th – Mar.6th 2020
R4-2002485

## Slide 2: Background
There are several definition related to each other for IAB TS in RAN4#94-e
IAB channel bandwidth
  R4-2002045
  R4-2000275
IAB DU/MT uplink and downlink related to the channel bandwidth definition
  R4-2001902

## Slide 3: Background (1st round summary)
Tentative agreements: No TS text can be drafted until we have more progress on sub topic 1-1. However there is some agreement that some unique text is needed in the channel BW section. Also it seems the method on referring to IAB channel BW needs some discussion. 0275 uses on “IAB channel bandwidth” whereas 2045 uses both IAB-DU channel bandwidth and IAB-MT channel bandwidth. This issue can be further discussed
Candidate options:
Recommendations for 2nd round: Further discuss the requirements for IAB channel BW in a WF

## Slide 4: Background
Though 0275 use ”IAB channel bandwidth”, in TP the different reference to BS channel bandwith or UE channel bandwidth means the IAB BW is different for IAB MT and IAB DU. The tricky thing is that when IAB DU and MT configured different bandwidth not the same, the general term of IAB channel bandwidth will cause ambiguity.
  Recommendation: Use ”IAB DU channel bandwidth” and ”IAB MT channel bandwidth” when defining sysem parameter

## Slide 5: Background
Referencing or self contained :
  For channel bandwidth, there are some text in generic description of BS channel bandwidth and UE bandwidth which need to be treated differently, for example, the meaning of the uplink and downlink for a UE is not the same for the IAB MT. For specific example:
    in 38.101-2 ,chapter 5.3.1, first phrase
      ” The UE channel bandwidth supports a single NR RF carrier in the uplink or downlink at the UE.”
    In 38.104,
    ” The BS channel bandwidth supports a single NR RF carrier in the uplink or downlink at the Base Station. Different UE channel bandwidths may be supported within the same spectrum for transmitting to and receiving from UEs connected to the BS. The placement of the UE channel bandwidth is flexible but can only be completely within the BS channel bandwidth. The BS shall be able to transmit to and/or receive from one or more UE Bandwidth parts that are smaller than or equal to the number of carrier resource blocks on the RF carrier, in any part of the carrier resource blocks.”

## Slide 6: Way forward
”IAB DU channel bandwidth” and ”IAB MT channel bandwidth” will be used for channel bandwidth chapter in IAB TS.
FFS on clarification of the ”uplink and downlink” in channel bandwdith chapter when drafting the TP for TS
FFS on self contained way to draft
  Channel bandwidth