## Slide 1: WF on enabling PC3 for NR-U in Rel-16
Charter Communications, Comcast, Cable Labs, Intel, Ericsson
R4-2002754
3GPP TSG-RAN WG4 Meeting #94-e
Electronic Meeting, Feb.24th – Mar.6th 2020

## Slide 2: Background
In [1], a summary was provided by the moderator from the email discussions in R4 #94e
  The proposal was to continue work on both PC5 and PC3
  Secondly, it was proposed as an option to use the same SEM definition for both PC5 and PC3
    Based on this proposal, the ACLR values for PC3 and PC5 should be identified
  Two PC3 configurations were discussed
      2 PA ( PC5+PC5)
      1 PA (PC3)
  With regards to Tx diversity power combining, what MPR/A-MPR spec will be needed?

## Slide 3: Background (2)
In previous meetings, there have also been several proposals which will be summarized below for reference.
  In [2], there was a proposal to use 27dBc for ACLR or 802.11ax SEM is used for 0 dB MPR calibration in PC5 using 20 MHz 100RB0 QPSK DFT-s-OFDM waveform
  In [3], there was a proposal for PA calibration and test procedure
  In [4], there was a proposal, based on 802.11ax spectrum mask, for ACLR for PC5 should be 26 dBc or 29dBc for PC3
  In [5], there were two proposals made:
    For PC5
      PC5 (20 dBm) , 27 dBc ACLR (equivalent to 802.11ax SEM) is used for 0 dB MPR calibration in PC5 using 20 MHz 100RB0 QPSK DFT-s-OFDM waveform and transceiver impairments are kept at 28 dBc image and carrier (and may need improvement for wideband operation)
    For PC3 , the following architectures should be studied:
      23 dBm single antenna, 23 dBm Coherent 2x2 UL MIMO using two PC5 paths, 23 dBm transparent Tx Diversity using two PC5 paths (for example using CDD)
      Reuse of NR 30 dBc ACLR limit as the definition for 0 dB MPR is FSS and relaxation may be studied
  In [6], there were two proposals to make ACLR spec of 30dBc for PC3 and 27dBc for PC5
  In [7], similar proposal as in [5] with additional details on waveform and Rb allocation
In summary, there is some common understanding that the same baseline SEM should be applied for both PC5 and PC3
There has been some proposals to align the ACLR spec with the SEM requirements
  27dBc for PC5 and 30dBc for PC3; Skyworks and Nokia
  26dBc for PC5 and 29dBc for PC3; Intel
  25.5 for PC5 ; Qualcomm

## Slide 4: Way Forward
PC3 power class is defined with 23 dBm maximum output power and max tolerance of +2/-3 dB
ACLR =[30dBc] for PC3
  Once simulations are available and reviewed, we can decide the final value
Companies are encouraged to identify a common architecture to enable PC3 ( Meeting #94e, Feb). Three proposals have been identified.
  Two PC5 Wi-Fi PA’s
  Tx diversity using two PC5 PA’s and power combining
  Single PA, PC3
Common agreement and understanding for PA calibration and test procedures should be reached in #94e ( Feb). There has been three proposals identified
    One proposal was identified in [3] by Qualcomm
    A second proposal was identified in [4] by Intel
    A third proposal was identified in [2] by Skyworks
Companies are encouraged to provide MPR and A-MPR simulations using architecture, the PA calibration and test procedures concluded in round 2 of #94 e-meeting in #94B e-meeting (April)

## Slide 5: References
[1] R4-2002684 Email discussion summary for RAN4#94e_#10_NR_unlic_UE_RF; Qualcomm
[2] R4-1905845 [NR-U] On NR-U Power Class, MPR and Channel Support, Skyworks
[3] R4-1907117 NR-U UE power class and PA calibration, Qualcomm
[4] R4-1908251 NR-U power class and ACLR requirement, Intel
[5] R4-1908844 [NR-U] On NR-U UE Power Class and MPR Evaluation, Skyworks
[6] R4-1911612 NR-U UE ACLR for PC3 and PC5, Nokia
[7] R4-1911614 [NR-U] UE Power Class Definitions, Skyworks
[8] R4-1912317 NR-U UE power class , Sony
[9] R4-1912490 Power class 3 for NR-U, Qualcomm
[10] R4-1913810 [NRU] Measurements for PC5 and PC3 Definition, Skyworks
[11] R4-1915983 On NRU UE Output Power, LG Electronics