## Slide 1: WF on MPR/A-MPR simulation assumptions and parameters for simultaneous PSFCH transmission
Agenda item: 8.4.4.1
Source: Huawei, HiSilicon
3GPP TSG-RAN WG4 Meeting #94-e R4-2002758
Electronic Meeting, Feb.24th – Mar.6th 2020

## Slide 2: Background
In last RAN4 #93 meeting and e-mail discussion, we discussed the basic simulation assumption of the required MPR levels for simultaneous PSFCH transmission of multiple feedbacks.
In RAN4#94e, companies provide the simulation results. There are two options for this sub-topic which is recorded in first round summary R4-2002685.
  Option1: Up to 5dB MPR for 2-5 user simultaneous PSFCH transmission with non-contiguous RB allocation.
  Option2: Proposed equation for MPR requirements (up to 10.1dB) for simultaneous PSFCH transmission with non-contiguous RB allocation.
In order to be aligned with each other, the simulation assumption and parameters for PSFCH are further proposed.

## Slide 3: Assumption and parameters
parameter | Assumption
center frequency | 2.7GHz/5.9GHz
Bandwidth | 10/20/30/40MHz
numerology | 15 kHz/30kHz/60kHz
Modulation for PSSCH | QPSK
PSFCH | ZC sequence
Waveform | CP-OFDM
Carrier leakage | 25dBc
IQ image | 25dBc
CIM3 | 45 or 60 dBc
PA calibration | Referring to PSSCH/PSCCH
Structure of Slot | Baseline is follow RAN1 agreements (if it is impact to derive MPR level, RAN4 will decide specific slot structure)

## Slide 4: RB allocation (1)
Both Non-contiguous PSFCH RB allocation and contiguous PSFCH allocation are allowed
  MPR will be derived by non-contiguous PSFCH RB allocation (N>1)
At least, the worst cases with possible RBstart and Ngap need to be checked. ( Ngap = RBend – RBstart )
  For example: The worst case N gap is (106-1 =105*15kHz*12=) 18.9MHz for 20MHz, 15kHz SCS
IMD problem by dual PSFCH in SEM/SE region shall be considered to derive MPR level according to all supporting CBW and SCS.
N (Number of users) is up to 5 and RBs except for RBstart and RBend can be inserted between RBstart and RBend randomly.
Assumption of N in RAN4 is only for MPR simulation purpose, the final number is up to RAN1 decision.

## Slide 5: RB allocation (2)
8 | 9 | 10 | 11 | … |  | 14
 |  |  |  |  |  | 13
 |  |  |  |  |  | 12
 |  |  |  |  |  | 11
 |  |  |  |  |  | 10
4 | 5 | 6 | 7 |  |  | 9
 |  |  |  |  |  | 8
 |  |  |  |  |  | 7
 |  |  |  |  |  | 6
 |  |  |  |  |  | 5
0 | 1 | 2 | 3 |  |  | 4
 |  |  |  |  |  | 3
 |  |  |  |  |  | 2
 |  |  |  |  |  | 1
 |  |  |  |  |  | 0
Ngap
RBstart
RBend
3 users

## Slide 6: Reference
R4-2001079 [V2X] TP on PSFCH MPR requirements for NR V2X in band n47, Huawei, HiSilicon
R4-2001719 MPR simulations results for multi-UE PSFCH transmission, LG Electronics
R4-2000704 On Simultaneous Transmission of PSFCH, Futurewei
R4-2000473 MPR, A-MPR results for simultaneous PSFCH transmission, Qualcomm Incorporated
R4-2001218 TP on revised MPR simulation assumptions and update NR requirements to cover open issue, LG Electronics
R4-2001215 Summary on E-mail discussion for NR V2X, LG Electronics