## Slide 1: WF on MPR requirement for intra-band contiguous UL CA
Huawei, HiSilicon, [Nokia],[Qualcomm],[Skyworks]…
R4-2002805
3GPP TSG-RAN WG4 #94e
Feb 24th – Mar 06th, 2020
Electric meeting

## Slide 2: Inner and outer RB allocation
Contiguous RB allocations:
For aggregated channel bandwidth≤100MHz, Inner RB allocation is defined with the equation:
For RBStart,Low = max(1, floor(NRB_alloc /2)), where NRB_alloc=LCRB1*2^µ1+LCRB2*2^µ2
Inner RB allocation is defined as RBStart,Low ≤ RBStart ≤ RBStart,High, NRB_alloc≤ceil[(1/2NRB,agg) ]
RBStart,High = NRB,agg – RBStart,Low – NRB,alloc, where NRB,agg=NRB1*2^µ1+ NRB1*2^µ2
RBStart = RBStart1 ∙ 2^m1, if LCRB1 > 0
RBStart = NRB1 ∙ 2^m1 + RBStart2∙2^m2, if LCRB1 = 0
For aggregated channel bandwidth>100MHz
  Option 1:
  For RBStart,Low = max(1, floor(NRB_alloc)), where NRB_alloc=LCRB1*2^µ1+LCRB2*2^µ2
  Inner RB allocation is defined as RBStart,Low ≤ RBStart ≤ RBStart,High, NRB_alloc≤Floor[(1/3NRB,agg) ]
  RBStart,High = NRB,agg – RBStart,Low – NRB,alloc, where NRB,agg=NRB1*2^µ1+ NRB1*2^µ2
For the case with only RBs configured in CC2, RBStart,Low and RBStart shall accounts for NRB1 in CC1
  Option 2: Same inner/outer allocation definition with bullet 2, but with a relaxed MPR.

## Slide 3
Inner and outer RB allocation
Non-Contiguous RB allocations:
Inner allocation: IMD3 falls within aggregated channel bandwidth, the equation will be further optimized in the next meeting to ensure IM3 would not leaking out of aggregated channel bandwidth based on the following formatcan be as below:
For RBStart,Low = max(1, floor(NRB_alloc)),
where NRB_alloc = LCRB2 ∙ 2^µ2, if LCRB1=0
NRB_alloc = LCRB1 ∙ 2^µ1, if LCRB2=0
NRB_alloc = (NRB1- RBStart1) ∙ 2^µ1 + (RBStart2+ LCRB2) ∙ 2^µ2, otherwise
Inner RB allocation is defined as RBStart,Low ≤ RBStart ≤ RBStart,High, NRB_alloc≤Floor[(1/3NRB,agg) ]
RBStart,High = NRB,agg – RBStart,Low – NRB,alloc, where NRB,agg=NRB1*2^µ1+ NRB2*2^µ2
RBStart = RBStart1 ∙ 2^m1, if LCRB1 > 0
Outer allocation:
  Option 1: further group into outer 1 and outer 2, where outer 2 means IM5 falls outside of the -13dBm/MHz SEM mask or in the -25dbm/MHz and -30dBm/MHz spurious region.
  Option 2: all allocations except inner allocation in bullet 1 is an outer allocation, take the worst MPR when defining MPR for outer allocation
  Option 3: all allocations except inner allocation in bullet 1 is an outer allocation, allow MPR to be reduced by the allocation ratio as was done for LTE CA.
  Option 4: further group into outer 1 and outer 2, allow MPR to be reduced by the allocation ratio as was done for LTE CA for outer 2 allocation

## Slide 4: MPR value: contiguous allocation
Modulation |  | MPR for bandwidth class B |  | MPR for bandwidth class C | 
 |  | inner | outer | inner | outer
DFT-s-OFDM | Pi/2 BPSK | TBD | TBD | TBD | TBD
 | QPSK | TBD | TBD | TBD | TBD
 | 16QAM | TBD | TBD | TBD | TBD
 | 64QAM | TBD | TBD | TBD | TBD
 | 256QAM | TBD | TBD | TBD | TBD
CP-OFDM | QPSK | TBD | TBD | TBD | TBD
 | 16QAM | TBD | TBD | TBD | TBD
 | 64QAM | TBD | TBD | TBD | TBD
 | 256QAM | TBD | TBD | TBD | TBD
For contiguous inner allocation, it is encouraged to further evaluate and provide simulation/measurement result on following RB allocation:
  20M+20M(15kHz+15kHz): large allocation , i.e. 53RB53+53RB0
  50M+50M(15kHz+15kHz): large allocation , i.e. 135RB135+135RB0
  100M+60M(30kHz+30kHz): large allocation , i.e. 54RB108+162RB0
  100M+100M(30kHz+30kHz): large allocation , i.e. 136RB137+136RB0
For contiguous Outer allocation, it is encouraged to further evaluate and provide simulation/measurement result on full RB allocations for ≤100MHz and >100MHz.

## Slide 5
MPR value: non-contiguous allocation
Modulation |  | MPR for bandwidth class B |  | MPR for bandwidth class C | 
 |  | inner | outer | inner | outer
DFT-s-OFDM | Pi/2 BPSK | TBD | TBD | TBD | TBD
 | QPSK | TBD | TBD | TBD | TBD
 | 16QAM | TBD | TBD | TBD | TBD
 | 64QAM | TBD | TBD | TBD | TBD
 | 256QAM | TBD | TBD | TBD | TBD
CP-OFDM | QPSK | TBD | TBD | TBD | TBD
 | 16QAM | TBD | TBD | TBD | TBD
 | 64QAM | TBD | TBD | TBD | TBD
 | 256QAM | TBD | TBD | TBD | TBD
For non-contiguous inner allocation, it is encouraged to further evaluate and provide simulation/measurement result on RB allocation with IMD5/7 falls into the SEM -13dBm/MHz
  20M+20M: i.e.1RB72+1RB31
  50M+50M: i.e. 1RB198+1RB94
  100M+60M: i.e. 1RB161+1RB132
  100M+100M : i.e. 1RB183+1RB87
For non-contiguous outer allocation, it is encouraged to further evaluate and provide simulation/measurement result on worst RB allocation case: 1RB+1RB for outer2 allocation
  20M+20M: i.e.1RB0+1RB105
  50M+50M: i.e.1RB0+1RB269
  100M+60M: i.e. 1RB0+1RB272
  100M+100M:i.e. 1RB0+1RB272
* Note: Whether Outer allocation need to be further grouped into 2 type depends on the conclusion in slide 3

## Slide 6
AMPR on NS04 and NS27
Currently de-prioritize the NS04 and NS27 in Rel-16 before MPR requirement is completed