## Slide 1: WF on Inter-band DL CA
Apple
3GPP TSG-RAN WG4 Meeting #94-e R4-2002825
#22_NR_RF_FR2_req_enh_Part_3
Electronic Meeting, Feb 24th – March 6th, 2020

## Slide 2: Background
In this meeting the following topics are being discussed:
Quantifying spherical coverage for inter-band CA, either:
  For each band determined separately, and common coverage area established
  Common CDF shall be used for LB + LB and common CDF shall not be used for LB + HB
For LB + LB, HB + HB, LB + HB:
  Capability signalling for PSD difference
  PSD difference
  Beam management (for LB + LB, HB + HB)
Separate L+H from L+L/H+H in WID
Testing consideration for inter-band CA

## Slide 3: WF on LB + LB, HB + HB
No capability signaling for DL PSD difference for LB + LB and HB + HB case
Equal PSD for LB + LB and HB + HB
Common Beam management

## Slide 4: WF on LB + HB
Two alternatives for PSD difference:
  Alternative 1: ≥ 25 dB and  30 dB
    If Alt. 1 is agreed, no capability signaling for DL PSD difference for LB + HB
  Alternative 2: 6.5 dB.
    If Alt. 2 is agreed, whether capability signaling for DL PSD difference is required for LB + HB is FFS
  Reference plane where PSD is defined is FFS.

## Slide 5: WF on LB + HB & L+L/H+H
EIS relaxation framework for both LL/HH and LH:
  Single band + MBR + inter-band DL CA relaxation factor.
  Values of inter-band DL CA relaxation factor for peak EIS and spherical EIS, respectively, are FFS
    How spherical coverage for inter-band related to the EIS relaxation is FFS