## Slide 1: Way Forward on MPR for PC1.5 UL MIMO and Tx div
T-Mobile USA
3GPP TSG-RAN WG4 Meeting #94-eBis R4-2005190
Electronic Meeting, 20-30 April 2020

## Slide 2: Background
A proposal for measurements assumptions for PC 1.5 UL MIMO and Tx Diversity was discussed [1]
Comments were collected in the e-mail discussion document [2].

## Slide 3: Background: WF to include
1) Measurement and simulation assumptions
2) EVM and IBE considered for MPR
3) Reference point for test
4) Branch or combined EVM for Tx diversity (per branch for UL MIMO)
5) Further study of high order modulations and wide allocations
6) Focus on Edge allocations and potential EVM issues due to RIMD
7) EVM budget for PA, image rejection, TRX and contribution for RIMD for different modulation order

## Slide 4: Proposal 1: Measurement and simulation assumptions for MPR and A-MPR
Antenna isolation of 10 dB
Post PA loss of 4 dB
Two 26 dBm Tx chains (NR)
Equal Power on both transmit chains
Various channel and allocation BWs, with focus on “worst case” allocations
RB size, allocation position, waveform, and modulation should be the same between two transmitters
Results for both CP-OFDM and DFT-S-OFDM are welcome, with the priority being CP-OFDM because it is expected to be worst case
Determine back-off required to meet OOBE, ACLR and EVM specifications
Goal is to take data from multiple sources and define A-MPR curves for PC1.5 UL MIMO and Transmit diversity accommodating different implementations

## Slide 5: EVM and IBE assumptions
Proposal 2: EVM and IBE to be considered
Proposal 3: Reference point for test:
The antenna connector for each
branch. In this figure, 1dB IL was
accounted for:
Proposal 4: EVM per branch for UL MIMO and for Tx Div.
Proposal 5: Include high order modulation and wide allocations
Proposal 6: Focus on Edge allocations and potential EVM issues due to RIMD
Proposal 7: Include EVM budget for PA, image rejection, TRX and contribution for RIMD for different modulation order
Proposal 8: Each PA is calibrated with DFT-s-OFDM QPSK 100RB0 waveform at 25dBm at the each antenna for 31dB ACLR.
Proposal 9: EVM should assume worst case image rejection of 28dB for QPSK/16QAM/64QAM and 34dB for 256QAM
Proposal 10: Performance impact to EVM due to different implementation of cyclic delay based on existing EVM requirement can be further analyzed. Issues identified in [3] can also be further studied.

## Slide 6: References
[1] R4-2004639, “Proposal for measurement and simulation assumptions for 29 dBm UL MIIMO and Tx diversity MPR and A-MPR,” T-Mobile USA
[2] R4-2005111, “Email discussion summary for [94e Bis][25] LTE_NR_B41_Bn41_PC29dBm,” Moderator (T-Mobile USA)
[3] R4-2004815, RIMD issues with two transmitters in PC1.5, Qualcomm