## Slide 1: WF on NR gNB positioning measurements and report mapping
Ericsson
3GPP TSG-RAN WG4 Meeting # 94-e-Bis
Electronic Meeting, April 20-30, 2020
Agenda: 6.8
R4-2005380

## Slide 2: Selection of option for gNB measurement accuracy requirements
FFS: gNB measurements for which accuracy shall be defined.
Candidate options:
  Option 1:
    Define accuracy for SRS-RSRP and gNB Rx-Tx time difference
  Option 2:
    Define accuracy for SRS-RSRP, gNB Rx-Tx time difference and UL RTOA

## Slide 3: Optionality of gNB accuracy requirements
FFS: whether gNB positioning measurement accuracy is optional or mandatory if gNB supports the positioning measurement.
Candidate options:
  Option 1:
    Mandatory for gNB to meet accuracy for supported positioning measurement
  Option 2:
    Optional for gNB to meet accuracy for supported positioning measurement

## Slide 4: Side conditions for gNB measurement accuracy
FFS: Side conditions (e.g. SINR) for defining gNB positioning measurement accuracy
Candidate options for deriving side conditions:
  Option 1:
    Side conditions based on clause 7.2 of TS 36.111
  Option 2:
    Select side conditions to meet accuracy for UE’s serving cell; SINR value is FFS
  Option 3:
    Select side conditions to meet accuracy for UE’s serving as well as neighbor cells; SINR value is FFS
Same side conditions shall be used for defining accuracy for different gNB positioning measurements.

## Slide 5: Beam configuration for gNB measurement accuracy
FFS: Antenna beam configuration assumption in gNB for defining gNB positioning measurement accuracy.
Candidate options:
  Option 1:
    Fixed antenna beams are assumed in gNB for deriving accuracy
  Option 2:
    Accuracy does not depend on antenna beam configuration in gNB

## Slide 6: PRS/SRS configurations for gNB measurement accuracy
FFS: whether the gNB positioning measurement accuracy is defined for all or subset of the PRS/SRS configurations
Candidate options:
  Option 1:
    Accuracy is defined for all PRS/SRS configurations.
  Option 2:
    Accuracy is defined for subset of PRS/SRS configurations.

## Slide 7: Applicability of gNB Rx-Tx accuracy under TA change
FFS: rule on applicability of gNB Rx-Tx accuracy under TA change
Candidate options:
  Option 1:
    gNB Rx-Tx accuracy applies provided that the UE transmit timing does not changes due to gNB sending TA during the measurement period.
  Option 2:
    Same rule related to TA change should apply for UE Rx-Tx time difference and gNB Rx-Tx time difference.
  Other options are not precluded.

## Slide 8: Accuracy for different BS types (1-C, 1-H, 1-O, 2-O)
FFS: whether gNB positioning measurement accuracy requirement depends on BS type (1-C, 1-H, 1-O, 2-O).
Candidate options:
  Option 1:
    Same accuracy requirement applies for all BS types
  Option 2:
    Accuracy requirement depends on BS type

## Slide 9: gNB Measurement Report Mapping
The measurement report mappings for the following gNB measurements are captured in the LS sent to RAN2/RAN3 in R4-2005381:
  gNB Rx-Tx time difference measurement
  UL RTOA
  SRS-RSRP
gNB differential report mapping:
  Common understanding: gNB differential report mapping for Rx-Tx time, RSRP, UL RTOA will not be defined by RAN4 unless it is introduced by RAN3.
  It is common understanding that RAN3 did not discuss it.