## Slide 1: WF on BS receiver requirements for NR-U
Nokia, Nokia Shanghai Bell
R4-2005478
3GPP TSG-RAN WG4 Meeting #94-e-Bis
Electronic Meeting, April 20th – 30th 2020

## Slide 2: Contributions for RAN4#94-e bis on NR-U BS Rx requirements
R4-2003814 | Updated summary of simulation results for NR-U BS Rx FRC | Nokia, Nokia Shanghai Bell
R4-2003815 | NR-U BS REFSENS and ICS requirements | Nokia, Nokia Shanghai Bell
R4-2003816 | NR-U BS Dynamic range requirement | Nokia, Nokia Shanghai Bell
R4-2004043 | NR-U BS RX Simulation Results | Ericsson
R4-2004044 | NR-U BS RF RX Requirements for 60 kHz SCS | Ericsson
R4-2003702 | NR-U BS REFSENSICS | Huawei, HiSilicon
R4-2003703 | NR-U BS dynamic range | Huawei, HiSilicon
R4-2004159 | simulation results for NR-U BS RX FRC | ZTE Corporation
R4-2004160 | NR-U BS RX REFSENS and dynamic range requirement | ZTE Corporation
R4-2004161 | NR-U BS RX ICS requirement | ZTE Corporation
R4-2004488 | NR-U BS REFSENS | Huawei, HiSilicon
R4-2004489 | NR-U BS dynamic range | Huawei, HiSilicon

## Slide 3: Background
During RAN4#93 meeting simulation assumptions for NR-U FRCs were agreed in [1]. Additionally during RAN4#94e meeting updated FRCs were agreed in [2].
Companies submitted for RAN4#94-e-bis SNR ssimulation results for NR-U FRCs and proposals for BS receiver requirements for NR-U.
This WF collect agreements on BS Rx requirements for NR-U done during RAN4#94-e-bis meeting.
[1] R4-1916162, WF on NR-U BS RF RX FRC, ZTE
[2] R4-2002465, WF on NR-U FRCs, Nokia, Nokia Shanghai Bell

## Slide 4
REFSENS and ICS FRC | Nokia | ZTE | Ericsson | Huawei | 
 | R4-2003814 | R4-2004159 | R4-2004043 | R4-2004488 | Average [dB]
G-FR1-A1-12 10MHz-15kHz-5PRBs | -0.70 | -0.72 | -0.25 | -0.21 | -0.5
G-FR1-A1-13 10MHz-30kHz-4PRBs | -0.50 | -0.55 | -0.15 | -0.07 | -0.3
G-FR1-A1-14 20MHz-15kHz-10PRBs | -0.90 | -0.93 | -0.45 | -0.42 | -0.7
G-FR1-A1-15 20MHz-30kHz-10PRBs | -0.90 | -0.93 | -0.45 | -0.42 | -0.7
G-FR1-A1-16 40MHz-15kHz-21PRBs | -1.00 | -1.09 | -0.60 | -0.60 | -0.8
G-FR1-A1-17 40MHz-30kHz-21PRBs | -1.00 | -1.09 | -0.60 | -0.61 | -0.8
G-FR1-A1-18 60MHz-30kHz-32PRBs | -1.20 | -1.27 | -0.75 | -0.74 | -1.0
G-FR1-A1-19 80MHz-30kHz-43PRBs | -1.20 | -1.28 | -0.80 | -0.77 | -1.0
Dynamic range FRC | Nokia | ZTE | Ericsson | Huawei | 
 | R4-2003814 | R4-2004159 | R4-2004043 | R4-2004489 | Average [dB]
G-FR1-A2-7 10MHz-15kHz-5PRBs | 9.10 | 9.15 | 9.20 | 9.39 | 9.2
G-FR1-A2-8 10MHz-30kHz-4PRBs | 9.10 | 9.24 | 9.25 | 9.41 | 9.3
G-FR1-A2-9 20MHz-15kHz-10PRBs | 9.00 | 9.07 | 9.15 | 9.37 | 9.1
G-FR1-A2-10 20MHz-30kHz-10PRBs | 9.00 | 9.07 | 9.15 | 9.37 | 9.1
G-FR1-A2-11 40MHz-15kHz-21PRBs | 8.80 | 8.90 | 9.00 | 9.17 | 9.0
G-FR1-A2-12 40MHz-30kHz-21PRBs | 8.80 | 8.90 | 9.00 | 9.17 | 9.0
G-FR1-A2-13 60MHz-30kHz-32PRBs | 8.80 | 8.90 | 9.00 | 9.15 | 9.0
G-FR1-A2-14 80MHz-30kHz-43PRBs | 8.70 | 8.83 | 8.95 | 9.14 | 8.9
Way forward
SNR results
Submitted by companies SNR simulation results for FRCs for 15 kHz and 30 kHz and CBWs 10/20/40/60/80 MHz are collected in table.
Agreement: To apply average SNR results to derive NR-U BS receiver requirements.

## Slide 5
BS Rx requirements for 60 kHz SCS
For 60 kHz SCS requirements, due to lack interlace design, legacy NR requirements values should be reused (REFSENSE, ICS, Dynamic Range).
Legacy NR requirements
Agreement: To reuse legacy 60 kHz NR Rx requirements NR-U BS for 10/20/40/60/80 MHz CBW: REFSENSE, In-channel selectivity, Dynamic range.
Way forward
Excerpt from the TS 38.104.

## Slide 6
BS Rx requirements for 15 kHz and 30 kHz SCS
Agreement: To derive following BS Rx requirements based on averaged simulation results (for 15kHz and 30kHz SCS):
    RESENSE
    In-channel selectivity
    Dynamic range
Way forward