## Slide 1: WF on IAB-MT Features
Qualcomm Incorporated
R4-2005483
3GPP TSG-RAN WG4 Meeting # 94-e-Bis
Electronic Meeting, 20 – 30 April, 2020

## Slide 2: Modulation related features
Feature group | Component | WF
1-1 | 60kHz of subcarrier spacing for FR1 | Optional
1-2 | 64QAM modulation for FR2 PDSCH | FFS Option 1. Mandatory Option 2: Optional with manufacturer declaration Note: LS can be sent to RAN1/RAN2 to check whether there are any issues for initial access if we take this feature as optional
1-3 | 64QAM for PUSCH | FFS Option 1. Mandatory Option 2: Optional with manufacturer declaration Note: LS can be sent to RAN1/RAN2 to check whether there are any issues for initial access if we take this feature as optional
1-4 | 256QAM for PDSCH | For FR1： Option 1. Mandatory Option 2: Optional with manufacturer declaration Note: LS can be sent to RAN1/RAN2 to check whether there are any issues for initial access if we take this feature as optional For FR2： Option 1: Optional with manufacturer declaration Option 2: Optional with capability signaling
1-5 | 256QAM for PUSCH | Option 1: Optional with manufacturer declaration Option 2: Optional with capability signaling

## Slide 3: Other Physical Layer Related Features
Handling of 1-8
  Send LS to RAN1/2 to clarify if there are any issues expected with initial access if DCI based switching delay is not specified
Feature group | Component | WF
1-6 | pi/2-BPSK for PUSCH | FFS Option 1: PI/2 BPSK not supported Option 2: Mandatory with capability for FR2, optional for FR1
1-7 | pi/2-BPSK for PUCCH format 3/4 | Option 1: PI/2 BPSK not supported Option 2: Mandatory with capability for FR2, optional for FR1
1-8 | Active BWP switching delay | Do not support this feature, send LS to RAN1/2 to clarify if there are any issues for initial access
1-11 | 7.5kHz UL raster shift | FFS
2-7 | Almost contiguous UL CP-OFDM | Optional

## Slide 4: Band Support Related Features
Feature 2-1
  RAN4 already sent an LS to RAN2 to inform about this agreement
Feature group | Component | WF
2-1 | Maximum channel bandwidth supported in each band for DL and UL separately and for each SCS that UE supports within a single CC | Optional, support through declaration.
2-8 | UE power class | FFS – to be discussed after IAB-MT class handling is clear
2-10 | Multiple frequency band indication | Not needed
2-11 | Modified MPR behaviour | FFS – to be discussed after MPR/A-MPR definition for IAB-MT is clear
2-12 | Multiple NS/P-Max | FFS – to be clarified after handling of NS values and MPR/A-MPR is clear
2-13 | Maximum uplink duty cycle for FR1 power class 2 UE | Not needed
2-14 | Power boosting for Pi/2 BPSK for power class 3 UE | FFS until support of handling of PI/2 BPSK is clarified
2-15 | Maximum uplink duty cycle for FR2 | Not needed

## Slide 5: CA and EN-DC support related features
Feature group | Component | Recommended WF
1-9 | Support of EN-DC with LTE-NR coexistence in UL sharing from UE perspective | FFS – to be discussed when a band with ULSUP is proposed for IAB-MT
1-10 | Switching time between LTE UL and NR UL for EN-DC with LTE-NR coexistence in UL sharing from UE perspective | FFS – to be discussed when a band with ULSUP is proposed for IAB-MT
2-2 | Simultaneous reception or transmission with same or different numerologies in CA | FFS – to be discussed when CA and EN-DC support framework is clear
2-3 | Non-contiguous intra-band CA frequency separation class for FR2 | FFS – to be discussed when CA and EN-DC support framework is clear
2-4 | Simultaneous reception and transmission for inter-band EN-DC (TDD-TDD or TDD-FDD) | FFS – to be discussed when CA and EN-DC support framework is clear
2-5 | Simultaneous reception and transmission for inter band CA (TDD-TDD or TDD-FDD) | FFS – to be discussed when CA and EN-DC support framework is clear
2-6 | Asynchronous FDD-FDD intra-band EN-DC | FFS – to be discussed when CA and EN-DC support framework is clear
2-9 | Simultaneous reception and transmission for SA SUL band combinations | FFS – to be discussed when CA and EN-DC support framework is clear
2-16 | PA architectures for intra-band EN-DC | FFS – to be discussed when CA and EN-DC support framework is clear
2-17 | PA architectures for intra-band UL CA | FFS – to be discussed when CA and EN-DC support framework is clear

## Slide 6: Baseband related features
Feature group | Component | Recommended WF
3-1 | Independent measurement gap configurations for FR1 and FR2 | Not supported
3-2 | Simultaneous reception of data and SS block with different numerologies when UE conducts the serving cell measurement or intra-frequency measurement | Optional
3-3 | Short measurement gap | Not supported
3-4 | SU-MIMO Interference Mitigation advanced receiver | Optional

## Slide 7: Other Issues
Send LS to RAN2 to inform that RAN4 agreed some Rel.15 features will not be supported for IAB-MT and this should be taken into account