## Slide 1: Way forward on PUSCH demodulation requirements for 30% throughput test point
3GPP TSG-RAN WG4 Meeting #94-e-bis
Electronic Meeting, Apr. 20th - 30th 2020
Agenda item: 6.18 [NR_perf_enh-Perf]
Document for: Approval
R4-2005551
CATT, …

## Slide 2: Background
Agreements and open issue in RAN4 #94-e based on [1]
    Agreements
    Define requirements for DM-RS 1+1 and 1+0, and conduct tests based on Rel-15 test applicability.
      Companies can provide simulation results for their interested cases.
    Define requirements for with and without PT-RS, and conduct tests based on Rel-15 test applicability.
      Companies can provide simulation results for their interested cases.
    Open issue
    Channel bandwidth
      Option 1: Add the 30% TP test cases with RBs for the minimum channel bandwidth per SCS (i.e., 25RB for 15kHz SCS, 24RB for 30kHz SCS, 66RB for 60kHz SCS, 32RB for 120kHz SCS, which are agreed in #92bis) to all tables for CP-OFDM (i.e., Table 8.2.1.2-1 – 8.2.1.2-14, Table 11.2.2.1.2-1 - 11.2.2.1.2-5 in TS 38.104, and corresponding Tables in TS38.141-1/2)
      Option 2: Add the 30% TP test cases with RBs for the minimum channel bandwidth per SCS (i.e., 25RB for 15kHz SCS, 24RB for 30kHz SCS, 66RB for 60kHz SCS, 32RB for 120kHz SCS, which are agreed in #92bis) to only tables for the minimum channel bandwidth per SCS for CP-OFDM (i.e., Table 8.2.1.2-1, 8.2.1.2-4, 8.2.1.2-8, 8.2.1.2-11, Table 11.2.2.1.2-1, 11.2.2.1.2-3 in TS 38.104, and corresponding Tables in TS 38.141-1/2)

## Slide 3: Agreements in the 1st round of RAN4#94-e-bis
PT-RS configurations
  Reuse R15 PT-RS configuration KPT-RS=2, LPT-RS=1 for NR PUSCH with 30% throughput test point.

## Slide 4: Way forward
  How to add 30% throughput test cases in specifications
  Option 1: Add the 30% TP test cases with RBs for the minimum channel bandwidth per SCS (i.e., 25RB for 15kHz SCS, 24RB for 30kHz SCS, 66RB for 60kHz SCS, 32RB for 120kHz SCS, which are agreed in #92bis) to the all tables for CP-OFDM (i.e., Table 8.2.1.2-1 – 8.2.1.2-14, Table 11.2.2.1.2-1 - 11.2.2.1.2-5 in TS 38.104, and corresponding Tables in TS38.141-1/2)
  Option 3a: New table for 30% TP test cases with RBs for the minimum channel bandwidth per SCS for CP-OFDM (i.e., 25RB for 15kHz SCS, 24RB for 30kHz SCS, 66RB for 60kHz SCS, 32RB for 120kHz SCS, which are agreed in #92bis) in TS38.104 and TS38.141-1/2. Option 4: Add a separate new table to capture performance requirements for 30% throughput and mandate its applicability.
  Agreement: Option 3a (based on the majority view).

## Slide 5: Way forward
  Whether to update applicability rules and how to specify if needed
  Option 1: To avoid misunderstanding, adding a statement in applicability rule and a note in each requirement table to clarity that 30% throughput requirement is only applied for the minimum PRBs for each subcarrier spacing declared to be supported. (Ericsson, ZTE)
  Option 2:
    Update the applicability of requirements for different subcarrier spacings in 8.1.2.1.1 of 38.141-1/2 to capture the previous agreement:
      Applicability rules
      SCS: Only test the lowest supported SCS for each frequency range
    No need to update the applicability of requirements for different channel bandwidths if adding new tables for 30% TP test cases is agreed.
  Agreement: Option 2.

## Slide 6: Way forward
DM-RS configurations
  Agreement: Keep the previous agreement.

## Slide 7: Way forward
Simulation results collection
  Companies are encouraged to carefully check the simulation results captured in this meeting. One more meeting is also needed for companies to further check or update the simulation results.

## Slide 8: Reference
[1] R4-2002397, Way forward on PUSCH demodulation requirements for 30% throughput, NTT DOCOMO, INC., RAN4#94-e
[2] R4-2005455, Email discussion summary for [94e Bis][225] NR_perf_enh_Demod_BS, CATT, RAN4#94-e
[3] R4-2002954, On channel bandwidth for 30% throughput PUSCH demodulation requirements, China Telecom, RAN4#94-e-bis
[4] R4-2002955, Simulation results for 30% throughput PUSCH demodulation requirements, China Telecom, RAN4#94-e-bis
[5] R4-2002972, Updated simulation results for Rel-16 performance enhancement, Samsung, RAN4#94-e-bis
[6] R4-2003273, Discussion on organization of PUSCH requirements with 30% throughput test point in specifications, CATT, RAN4#94-e-bis
[7] R4-2003274, Simulation results for NR PUSCH with 30% throughput test point, CATT, RAN4#94-e-bis
[8] R4-2003445, Discussion on Structure and applicability rule for 30% TP test point, Ericsson, RAN4#94-e-bis
[9] R4-2003545, Summary of ideal and impairment results for NR PUSCH with 30% throughput test point, CATT, RAN4#94-e-bis
[10] R4-2003627, Remaining issues on PUSCH 30% TP test point, NTT DOCOMO, INC., RAN4#94-e-bis
[11] R4-2003700, Disc on NR PUSCH 30percent TP perf capturing, Huawei, HiSilicon, RAN4#94-e-bis
[12] R4-2003701, Simulation results for NR Rel-16 BS performance requirements for 30% TP test pointHuawei, HiSilicon, RAN4#94-e-bis
[13] R4-2003896, On NR Rel-16 performance requirement enhancement BS demodulation 30% TP test poin, Nokia, Nokia Shanghai Bell, RAN4#94-e-bis
[14] R4-2003897, NR Rel-16 performance requirement enhancement BS demodulation simulation results, Nokia, Nokia Shanghai Bell, RAN4#94-e-bis
[15] R4-2003954, On Rel-16 demodulation requirements for 30% throughput testing points, ZTE Wistron Telecom AB, RAN4#94-e-bis
[16] R4-2003275, Draft CR for TS 38.104: Introduce PUSCH performance requirements at 30% throughput test point, CATT, RAN4#94-e-bis
[17] R4-2003276, Draft CR for TS 38.141-1: Introduce PUSCH performance requirements at 30% throughput test point, CATT, RAN4#94-e-bis
[18] R4-2003277, Draft CR for TS 38.141-2: Introduce PUSCH performance requirements at 30% throughput test point, CATT, RAN4#94-e-bis