## Slide 1: WF on MPR With PI/2 BPSK DMRS
Qualcomm
3GPP TSG-RAN WG4 NR #94-e-Bis
24th - 30th Apr 2020
R4-2005651

## Slide 2: Open Issues
Issue 1-1-1: Rel-15 MPR requirement for Pi/2 BPSK
  Proposal 1 (Huawei): Revisit firstly before consider whether MPR improvement based on Pi/2 BPSK DMRS should be defined in Rel-16
  Proposal 2 (Qualcomm): FFS further optimization of MPR for ZC based DMRS; this evaluation can proceed in parallel under the TEI WI.
Issue 1-1-2: Rel-16 MPR requirement for Pi/2 BPSK
  Proposal 1 (Huawei): If Rel-15 MPR for Pi/2 BPSK cannot be revised, then there is no RF requirements should be specified for new DMRS design, based on following observations:
    MPR can be improved a little bit for Pi/2 BPSK DMRS with FDSS compared to ZC DMRS with FDSS, but not too much
    The MPR improvement even with newly designed DMRS sequence cannot reach the power boosting level defined in Rel-15 spec
  Proposal 2 (Qualcomm): Pi/2 BPSK DMRS can be treated as a separate specification in the MPR tables (but MPR number can be discussed).

## Slide 3: Background (1)
Rel-15:
  MPR values for Pi/2 BPSK waveforms having Zadoff-Chu (ZC) modulated DMRS was agreed for both FR1 and FR2 and placed in the 38.101 specification.
  The full benefit of BPSK could not be realized due to the DMRS of these waveforms being a higher PAPR ZC modulation.
Revised Rel-16 WID on NR eMIMO (RP-192271) states:
  Perform study and make conclusion in the first RAN1 meeting after start of the WI, and if needed, specify CSI-RS and DMRS (both downlink and uplink) enhancement for PAPR reduction for one or multiple layers (no change on RE mapping specified in Rel-15)
  Specify core requirements associated with the items specified by RAN1 [RAN4]
    Identify impact on RF requirements for the reduced PAPR pi/2-BPSK DMRS and, if needed, specify RF requirements
Based on RP-192271 a new Pi/2 BPSK DMRS was created for use with Pi/2 BPSK modulated data that has lower PAPR

## Slide 4: Background (2) - Positions of each company
Company |  | 
 | Issue 1-1-1: Rel-15 MPR requirement for Pi/2 BPSK | Issue 1-1-2: Rel-16 MPR requirement for Pi/2 BPSK
Intel | Proposal 2. Need RAN4 approves it as a Rel-15 TEI | Proposal 2
Huawei | Rel-15 MPR requirement is connected with the newly designed DMRS sequence. If the requirement is over defined, we need to consider the possible improvement based on a correct basis | Rel-15 MPR requirement is connected with the newly designed DMRS sequence. If the requirement is over defined, we need to consider the possible improvement based on a correct basis
Qualcomm | We would like to stick to WID wording without increasing WI scope: ‘Identify impact on RF requirements for the reduced PAPR pi/2-BPSK DMRS for FR1 and, if needed, specify RF requirements’. Changing MPR for pi/2 BPSK carried over from rel-15 can take place once there is a WI driving it | We think that Pi/2 BPSK DMRS with FDSS should be specified in the mpr tables under a separate specification as it is a new DMRS scheme and it does provide palpable benefits. Why must Pi/2 BPSK DMRS achieve Rel-15 power boost levels for mpr improvement to be viable? There are other intermediate targets with tangible benefits.
Samsung | Based on WID, “Identify impact on RF requirements for the reduced PAPR pi/2-BPSK DMRS for FR1 and, if needed, specify RF requirements”, by this meeting, we need to identify the impact otherwise we need to make the clear conclusion that MPR requirement for Pi/2 BPSK DMRS will not be introduced. Whether Rel-15 power boosting requirement for Pi/2 BPSK needs revisit or not can be discussed in Rel-15 TEI to correct existing requirement if needed, but it is out of scope of Rel-16 eMIMO WI. | 
Nokia |  | Based on our studies presented in R4-2000517 we believe that REL-16 PI/2 PBSK MPR can be improved. This can be done by complementing current MPR table. Improvement and shaping should be further discussed. Enhancement should apply to both FR1 and FR2.

## Slide 5: WF on Pi/2 BPSK DMRS
The purpose of WI RP-192271 was to “Identify impact on RF requirements for the reduced PAPR pi/2-BPSK DMRS and, if needed, specify RF requirements”
Therefore, the following suggestions on the WF are made:
Proposal :
  Limit study to IE powerBoostPi2BPSK set to 0 and companies are encouraged to bring results in RAN4#95e to further evaluate the possibility of MPR enhancement for the new waveform configuration (pi/2 BPSK DMRS with pi/2 BPSK data) in Rel-16
  In RAN4#95e, RAN4 should conclude that whether or not the impact is idenfied on RF requirements for the reduced PAPR pi/2-BPSK DMRS.