## Slide 1: WF on adding 25MHz and 50MHz channel BW in band n1
Huawei
3GPP TSG-RAN WG4 Meeting #94-e-Bis
Electronic Meeting, 20 – 30 Apr., 2020
R4-2005185

## Slide 2: Agreements
A-MPR regions in Table 1 and Table 2 are agreed for 50 MHz channel BW.
Table 1: A-MPR regions for B39/B34 protection
Table 2: A-MPR regions for B33/B34 protection
  It is proposed to specify the A-MPR for each region for next meeting.
Channel Bandwidth, MHz | Carrier Center Frequency, Fc, MHz | Regions |  | A-MPR
 |  | RBend*12*SCS MHz | LCRB*12*SCS MHz | 
50 MHz | 1945 ≤ FC ≤ 1955 | ≥7.74, <14.4 | <1.08, [<max(0, 12*SCS*RBend – 7.74)] | FFS
 |  | ≥36, <39.6 | <1.08 | FFS
 |  | <39.6 | ≥18, <max (0, 12*SCS*RBend – 7.74) | FFS
 |  | <39.6 | ≥max (0, 12*SCS*RBend – 7.74) | FFS
 |  | ≥39.6 | >0 | FFS
Channel Bandwidth, MHz | Carrier Center Frequency, Fc, MHz | Regions |  | A-MPR
 |  | RBend*12*SCS MHz | LCRB*12*SCS MHz | 
50 MHz | 1945 ≤ FC ≤ 1955 | [≥0, <6.12] | [>0] | FFS
 |  | [≥6.12, <20.7] | [≥max (0, 12*SCS*RBend - 3.6)] | FFS
 |  | [≥20.7, <41.04] | [≥17.1] | FFS
 |  | [≥33.84, <41.04] | [<1.08] | FFS
 |  | [≥41.04] | [>0] | FFS

## Slide 3: References
[1] R4-2000108, n1 AMPR for 50MHz Channel BW, Qualcomm Incorporated
R4-2004493, A-MPR simulation results for n1 50MHz, Huawei, HiSilicon
R4-2004692, AMPR for n1 with 50MHz, Apple Inc.
R4-2004818, n1 50MHz REFSENS and Band n34 Protection Measurements, Skyworks Solutions Inc.